# Sediment Hydrocarbons

Hydrocarbon concentrations at each SDX-5 sample station were determined from 2 replicate sediment samples. Replicate values are given in Table 4.1. GC chromatograms are presented in appendix 4 and full PAH data is given in appendix 5. Agreement between replicate values at each station was generally very good.

Table 4.1 Replicate Hydrocarbon Concentrations SDX-5 Post Drill Survey 2010

| Sample ID | Replicate No | THC μg.g-1 | LAO μg.g-1 | % LAO | THC-LAO μg.g-1 | UCM μg.g-1 | % UCM | Total 2-6 ring PAH ng.g-1 | NPD ng.g-1 | % NPD | Total EPA 16 PAH ng.g-1 | Phenols μg.g-1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 234 | - | - | 234 | 169 | 73 | 1687 | 903 | 54 | 298 | 1.37 |
|  | 2 | 255 | - | - | 255 | 188 | 74 | 1687 | 843 | 50 | 323 | 1.93 |
| 2 | 1 | 308 | - | - | 308 | 227 | 74 | 1944 | 965 | 50 | 354 | 2.51 |
|  | 2 | 173 | - | - | 173 | 126 | 73 | 1151 | 585 | 51 | 199 | 3.25 |
| 3 | 1 | 257 | - | - | 257 | 187 | 73 | 1697 | 852 | 50 | 314 | 2.98 |
|  | 2 | 225 | - | - | 225 | 166 | 74 | 1586 | 799 | 50 | 300 | 2.47 |
| 4 | 1 | 303 | - | - | 303 | 222 | 73 | 2068 | 1068 | 52 | 378 | 2.13 |
|  | 2 | 415 | 49 | 12 | 366 | 268 | 65 | 2433 | 1245 | 51 | 440 | 3.16 |
| 6 | 1 | 246 | - | - | 246 | 180 | 73 | 1855 | 958 | 52 | 367 | 2.35 |
|  | 2 | 255 | - | - | 255 | 186 | 73 | 1985 | 1021 | 51 | 387 | 2.50 |
| 7 | 1 | 238 | - | - | 238 | 174 | 73 | 1554 | 777 | 50 | 284 | 3.17 |
|  | 2 | 271 | - | - | 271 | 196 | 72 | 1950 | 990 | 51 | 365 | 3.20 |
| 8 | 1 | 1336 | 550 | 41 | 786 | 577 | 43 | 679 | 548 | 81 | 56 | 0.75 |
|  | 2 | 1109 | 405 | 37 | 704 | 477 | 43 | 617 | 492 | 80 | 58 | 0.38 |
| 9 | 1 | 118 | - | - | 118 | 87 | 74 | 690 | 353 | 51 | 121 | 1.64 |
|  | 2 | 141 | - | - | 141 | 105 | 74 | 889 | 442 | 50 | 165 | 0.68 |
| 11 | 1 | 130 | - | - | 130 | 94 | 73 | 774 | 387 | 50 | 145 | 1.01 |
|  | 2 | 174 | - | - | 174 | 127 | 73 | 1131 | 572 | 51 | 213 | 1.46 |
| 12 | 1 | 315 | - | - | 315 | 235 | 75 | 2242 | 1125 | 50 | 422 | 1.78 |
|  | 2 | 214 | - | - | 214 | 165 | 77 | 1654 | 860 | 52 | 327 | 2.85 |
| 13 | 1 | 198 | - | - | 198 | 148 | 75 | 1436 | 718 | 50 | 248 | 1.40 |
|  | 2 | 233 | - | - | 233 | 172 | 74 | 1575 | 789 | 50 | 301 | 2.06 |
| 14 | 1 | 338 | - | - | 338 | 251 | 74 | 2184 | 1075 | 49 | 410 | 0.99 |
|  | 2 | 219 | - | - | 219 | 163 | 75 | 1503 | 767 | 51 | 279 | 2.02 |
| 15 | 1 | 199 | - | - | 199 | 144 | 72 | 1204 | 599 | 50 | 228 | 0.41 |
|  | 2 | 103 | - | - | 103 | 77 | 75 | 528 | 289 | 55 | 89 | 0.77 |
|  | Min | 103 | 49 | 12 | 103 | 77 | 43 | 528 | 289 | 49 | 56 | 0.38 |
|  | Max | 1336 | 550 | 41 | 786 | 577 | 77 | 2433 | 1245 | 81 | 440 | 3.25 |
|  | Median | 236 | 405 | 37 | 236 | 173 | 73 | 1581 | 794 | 51 | 299 | 1.98 |
|  | Mean | 308 | 335 | 30 | 269 | 197 | 71 | 1489 | 770 | 53 | 272 | 1.89 |
|  | St Dev | 280 | 258 | 16 | 155 | 110 | 8 | 545 | 257 | 8 | 112 | 0.92 |
|  | %CV | 91 | 77 | 53 | 58 | 56 | 12 | 37 | 33 | 15 | 41 | 49 |

Table 4.2 Hydrocarbon Summary Statistics excluding samples where LAO is present.

|  | THC μg.g-1 | LAO μg.g-1 | % LAO | THC-LAO μg.g-1 | UCM μg.g-1 | % UCM | Total 2-6 ring PAH ng.g-1 | NPD ng.g-1 | % NPD | Total EPA 16 PAH ng.g-1 | Phenols μg.g-1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Min | 103 | 0 | 0 | 103 | 77 | 72 | 528 | 289 | 49 | 89 | 0.41 |
| Max | 338 | 0 | 0 | 338 | 251 | 77 | 2242 | 1125 | 55 | 422 | 3.25 |
| Median | 233 | 0 | 0 | 233 | 169 | 74 | 1586 | 799 | 50 | 300 | 2.02 |
| Mean | 224 | 0 | 0 | 224 | 165 | 74 | 1521 | 771 | 51 | 283 | 1.95 |
| St Dev | 63 | 0 | 0 | 63 | 47 | 1 | 481 | 243 | 1 | 94 | 0.85 |
| %CV | 28 | 0 | 0 | 28 | 28 | 1 | 32 | 31 | 3 | 33 | 44 |

## LAO Linear Alpha Olefin

The presence of linear alpha olefin (LAO) synthetic hydrocarbons were detected in samples from stations 4 and 8. These forms of synthetic hydrocarbons are the base constituent of synthetic drilling fluid, the signature of which indicates the extent of contamination from the discharge of these types of drilling fluids.

Section 1.6 gives the drilling discharge data from the SDX-5 location. It has been reported that water based drilling fluids (WBM) were used in drilling operations at SDX-5 with no discharge or spill of synthetic (LAO) based mud. However, it is noted in the project environmental Technical Note (AETC 2007) that the use of SBM systems was planned for drilling the lower hole sections of the SDX-5 well.

As an LAO signature is present, this may indicate the presence of an unreported spill or accidental discharge of LAO drilling mud or LAO contaminated drill cuttings.

LAO concentrations of 550 and 405μg.g-1 were recorded in samples taken at station 8 adjacent to the drill site. LAO was also present at station 4 replicate 2 located 200m south of the drill site, the concentration was low with 49μg.g-1.

The position of stations 4 and 8 where LAO was present is given in figure 4.1 below; these have been given a red station marker.

Figure 4.1	Stations with LAO Signature.

Examination of the other measured parameters within these samples indicates that the concentrations of 2-6 ring PAH were within the ranges recorded in samples where LAO was absent. However, the concentration of USEPA 16 PAH at station 8 was lower with 56 and 58μg.g-1 with a higher proportion of NPD of 80 and 81%. These results are in comparison to USEPA 16 PAH of 89-422μg.g-1 and an NPD proportion of 49-55%.

Table 4.2 gives the summary statistics excluding samples 4R2, 8R1 and 8R2 where LAO was present and will be used in the following description of results.

## Total Hydrocarbons

Excluding samples were LAO was present, variation between THC concentrations was low with a %CV of 28. Concentrations ranged from 103 – 338μg.g-1 at stations 15R2 and 14R1 respectively with a median of 233 and a mean of 224μg.g-1. UCM represented a constant proportion of THC, ranging from 72-77%.

## Polynuclear aromatic hydrocarbons

When the samples containing LAO were excluded, the variation between PAH concentrations was low with a CV of 32%. Concentrations ranged from 528ng.g-1 at station 15R2 to 2242ng.g-1 at station 12R1. The median and mean concentrations were 1586 and 1521ng.g-1 respectively. As noted above the NPD proportion of 2-6 ring PAH was constant at 49-55% in samples where LAO was not present.

USEPA 16 PAH represented a constant proportion of 2-6 ring PAH and ranged from 89 to 422ng.g-1 at stations 15R2 and 12R1 respectively, with median and mean concentrations of 300 and 283ng.g-1.

## Phenols

Variation in phenol concentrations was highest with a CV of 44%, with concentrations ranging from 0.41 to 3.25g.g-1 at stations 15R1 and 2R2 respectively. The respective median and mean concentrations were 2.02 and 1.95μg.g-1.

## Relationship between Hydrocarbon Parameters

The relationship between measured parameters was tested by a Pearson’s r correlation analysis of the replicate data. The analysis was carried out excluding samples 4R2, 8R1 and 8R2, which have been shown to have different characteristics.

The results of the analysis are presented in table 4.3 below. With the exception of phenols strong relationships (>0.95) have been shown to exist between all measured parameters, the strength of which can be seen when the paired variables are plotted (Figure 4.2).

The paired variable scatter plot for THC and phenol is given in figure 4.3, which indicates that the presence of both parameters are independent.

Table 4.3	Correlation between Replicate Hydrocarbon Concentrations; SDX-5 Post Drill Survey 2010

|  | THC | UCM | % UCM | 2-6 ring PAH | NPD | % NPD | USEPA 16 PAH | Phenols |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| THC μg.g-1 | 1.00 |  |  |  |  |  |  |  |
| UCM μg.g-1 | 1.00 | 1.00 |  |  |  |  |  |  |
| % UCM | 0.05 | 0.10 | 1.00 |  |  |  |  |  |
| 2-6 ring PAH | 0.97 | 0.97 | 0.11 | 1.00 |  |  |  |  |
| NPD | 0.95 | 0.95 | 0.11 | 1.00 | 1.00 |  |  |  |
| % NPD | -0.06 | -0.06 | 0.01 | 0.11 | 0.18 | 1.00 |  |  |
| USEPA 16 PAH | 0.95 | 0.95 | 0.13 | 0.99 | 0.99 | 0.11 | 1.00 |  |
| Phenols | 0.28 | 0.28 | -0.02 | 0.36 | 0.37 | 0.23 | 0.35 | 1.00 |

Figure 4.2 Paired variable Scatter plots

Figure 4.3 Paired variable Scatter plot THC & Phenol

## Comparison to Previous Survey Data

Table 4.4 gives the comparable averaged hydrocarbon concentrations from the 2007 baseline survey and the 2010 post drill survey.

As noted LAO was detected at stations 4 and 8, the presence of which has elevated the THC concentration from the levels recorded in 2007, particularly at station 8. The proportion of NPD is also higher at station 8 in 2010, increasing from 52-80%.

Although the THC and PAH concentrations were slightly higher in 2010, in general the differences in average concentrations at each station were within the limits expected from sampling and analytical variation. The greatest difference was observed at stations 6, 12 and 14 with respective THC concentrations increasing from 119-251μg.g-1, 139-265μg.g-1 and 152-278 μg.g-1.

The range, median and mean phenol concentrations are lower in 2010. The greatest difference between years was the lower average concentrations at stations 8 and 15, reducing from 3.50-0.57μg.g-1 and 2.55-0.59μg.g-1 respectively.

Table 4.5 below gives the 2007 and 2009 hydrocarbon concentrations at Shah Deniz Regional stations 31 and 32, which are located in a similar position and depth to the SDX-5 stations.

When the SDX-5 data excluding stations 4 and 8 is compared to the data from Regional stations 31 and 32, THC and PAH concentrations are slightly higher at SDX-5. SDX-5 phenol concentrations are within the range recorded at SD stations 31 and 32 and the proportion of UCM and NPD are similar.

## Hydrocarbon Summary

The presence of synthetic LAO based hydrocarbons was detected in samples from stations 4 and 8, with the highest concentrations being present at stations 8. The characteristics of the hydrocarbon content at station 8 differed to all other stations, with a higher proportion of NPD and a lower concentration of USEPA16 PAH.

The detection of LAO in samples usually indicates the presence of contamination from discharged synthetic drilling fluids (SBM).

It has been reported that no discharge or spill of SBM have taken place at the SDX-5 location. However, it has been noted in the EIA technical note that the lower hole sections of the well would be drilled using an SBM system, which suggests that an unreported discharge or spill of SBM or SBM contaminated drill cuttings has taken place.

As LAO drilling mud does not contain PAH’s, the higher NPD proportion in samples from station 8 likely indicate the presence of cuttings contaminated with LAO drilling mud and also reservoir fluids.

At the remaining stations where LAO was not detected variation between hydrocarbon concentrations was low for all measured parameters. The respective concentration of UCM and NPD was universally high and low throughout, indicating that all hydrocarbons present were heavily weathered.

All measured parameters were related, with the exception of phenol concentrations which were found to be independent of all other compounds. This was also observed in the 2007 baseline study.

In general the THC and PAH concentrations were similar to those recorded on the 2007 baseline survey. The greatest difference was recorded at stations 6, 12 and 14, where concentrations were higher in 2010.

When compared to the data collected from Shah Deniz Regional Survey stations from a similar depth and position, the SDX-5 THC and PAH concentrations are slightly higher, phenol concentrations are within the SD regional range and the proportion of UCM and NPD are similar.

Table 4.4	Average Hydrocarbon Concentrations SDX-5 Baseline Survey 2007 & Post Drill Survey 2010

| Station | LAO μg.g-1 | THC μg.g-1 | UCM μg.g-1 | UCM, % | Total 2-6 ring PAH ng.g-1 | NPD ng.g-1 |
| --- | --- | --- | --- | --- | --- | --- |
|  | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 |
| 1 | ND | ND | 189 | 244 | 133 | 178 | 71 | 73 | 1117 | 1687 | 573 | 873 |
| 2 | ND | ND | 145 | 240 | 97 | 176 | 68 | 73 | 1040 | 1548 | 555 | 775 |
| 3 | ND | ND | 168 | 241 | 120 | 176 | 72 | 73 | 1042 | 1641 | 549 | 825 |
| 4 | ND | 25 | 239 | 359 | 173 | 245 | 73 | 69 | 1374 | 2251 | 723 | 1157 |
| 6 | ND | ND | 119 | 251 | 83 | 183 | 70 | 73 | 757 | 1920 | 405 | 990 |
| 7 | ND | ND | 206 | 254 | 153 | 185 | 75 | 73 | 1129 | 1752 | 577 | 884 |
| 8 | ND | 478 | 126 | 1222 | 94 | 527 | 74 | 43 | 833 | 648 | 433 | 520 |
| 9 | ND | ND | 163 | 129 | 119 | 96 | 73 | 74 | 1114 | 790 | 535 | 398 |
| 11 | ND | ND | 129 | 152 | 97 | 111 | 74 | 73 | 948 | 952 | 459 | 479 |
| 12 | ND | ND | 139 | 265 | 108 | 200 | 78 | 76 | 799 | 1948 | 373 | 993 |
| 13 | ND | ND | 148 | 216 | 116 | 160 | 78 | 74 | 867 | 1506 | 414 | 754 |
| 14 | ND | ND | 152 | 278 | 119 | 207 | 78 | 74 | 867 | 1844 | 425 | 921 |
| 15 | ND | ND | 152 | 151 | 119 | 110 | 78 | 74 | 1035 | 866 | 469 | 444 |
| Min | ND | 25 | 119 | 129 | 83 | 96 | 68 | 43 | 757 | 648 | 373 | 398 |
| Max | ND | 949 | 239 | 1222 | 173 | 527 | 78 | 76 | 1374 | 2251 | 723 | 1157 |
| Median |  |  | 152 | 244 | 119 | 178 | 74 | 73 | 1035 | 1641 | 469 | 825 |
| Mean |  |  | 160 | 308 | 118 | 197 | 74 | 71 | 994 | 1489 | 499 | 770 |
| ST Dev |  |  | 34 | 281 | 25 | 108 | 3 | 9 | 171 | 509 | 97 | 240 |
| %CV |  |  | 21 | 91 | 21 | 55 | 5 | 12 | 17 | 34 | 19 | 31 |

ND: Not detected

Table 4.4	Average Hydrocarbon Concentrations SDX-5 Baseline Survey 2007 & Post Drill Survey 2010 Continued

| Station | % NPD | Total EPA 16 PAH ng.g-1 | Phenols μg.g-1 |
| --- | --- | --- | --- |
|  | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 |
| 1 | 51 | 52 | NA | 311 | 1.49 | 1.65 |
| 2 | 54 | 50 | NA | 276 | 4.97 | 2.88 |
| 3 | 53 | 50 | NA | 307 | 3.39 | 2.72 |
| 4 | 53 | 51 | NA | 409 | 4.71 | 2.65 |
| 6 | 54 | 52 | NA | 377 | 2.25 | 2.42 |
| 7 | 51 | 50 | NA | 324 | 5.13 | 3.18 |
| 8 | 52 | 80 | NA | 57 | 3.50 | 0.57 |
| 9 | 48 | 50 | NA | 143 | 3.16 | 1.16 |
| 11 | 49 | 50 | NA | 179 | 3.80 | 1.24 |
| 12 | 47 | 51 | NA | 374 | 3.87 | 2.32 |
| 13 | 49 | 50 | NA | 275 | 3.61 | 1.73 |
| 14 | 49 | 50 | NA | 344 | 2.69 | 1.51 |
| 15 | 45 | 52 | NA | 162 | 2.55 | 0.59 |
| Min | 45 | 50 | NA | 57 | 1.49 | 0.57 |
| Max | 54 | 80 | NA | 409 | 5.13 | 3.18 |
| Median | 51 | 50 |  | 307 | 3.50 | 1.73 |
| Mean | 50 | 53 |  | 272 | 3.47 | 1.89 |
| ST Dev | 3 | 8 |  | 106 | 1.07 | 0.87 |
| %CV | 5 | 15 |  | 39 | 31 | 46 |

NA: No Analysis

Table 4.5	Average 2007 & 2009 Hydrocarbon Concentrations at SD Regional Stations 31 & 32

|  | THC μg.g-1 | UCM % | Total 2-6 ring PAH ng.g-1 | NPD ng.g-1 |
| --- | --- | --- | --- | --- |
| Station | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 |
| 31 | 121 | 155 | 86 | 74 | 822 | 938 | 296 | 508 |
| 32 | 116 | 168 | 76 | 72 | 1040 | 876 | 349 | 427 |

Table 4.5	Average 2007 & 2009 Hydrocarbon Concentrations at SD Regional Stations 31 & 32 Continued

|  | % NPD | USEPA 16 PAH ng.g-1 | Phenols µg.g-1 |
| --- | --- | --- | --- |
| Station | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 |
| 31 | 36 | 54 | NA | 155 | 3.02 | 4.56 |
| 32 | 34 | 49 | NA | 167 | 2.42 | 3.49 |

NA: No Analysis