# Metals in Sediments

Metal concentrations at each SDX-5 sample station were determined from 2 replicate sediment samples. Replicate values are given in Table 5.1.

Table 5.1 Replicate Metal Concentrations SDX-5 Post Drill Survey 2010 μg.g-1 dry sediment

| Station | Rep | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | R1 | 4.2 | 687 | 805 | 0.21 | 59.8 | 37.8 | 0.09 | 36,700 | 790 | 25.4 | 104 |
|  | R2 | 6.8 | 694 | 823 | 0.19 | 63.7 | 38.8 | 0.11 | 38,100 | 798 | 26.6 | 97 |
| 2 | R1 | 8.3 | 815 | 982 | 0.25 | 70.5 | 42.8 | 0.11 | 40,400 | 908 | 28.0 | 108 |
|  | R2 | 4.9 | 724 | 875 | 0.25 | 64.8 | 41.3 | 0.15 | 39,500 | 842 | 27.5 | 107 |
| 3 | R1 | 7.2 | 1,900 | 2,170 | 0.25 | 54.9 | 36.1 | 0.10 | 34,600 | 739 | 24.8 | 89 |
|  | R2 | 6.4 | 1,750 | 1,980 | 0.27 | 63.7 | 40.9 | 0.10 | 38,900 | 827 | 27.8 | 100 |
| 4 | R1 | 3.2 | 791 | 923 | 0.23 | 67.7 | 41.8 | 0.11 | 41,200 | 867 | 27.4 | 109 |
|  | R2 | 7.3 | 842 | 945 | 0.24 | 64.3 | 39.7 | 0.10 | 40,900 | 867 | 27.1 | 104 |
| 6 | R1 | 6.4 | 823 | 892 | 0.23 | 68.0 | 43.1 | 0.11 | 40,200 | 892 | 28.0 | 109 |
|  | R2 | 3.8 | 725 | 869 | 0.20 | 62.6 | 39.2 | 0.10 | 39,200 | 864 | 26.5 | 100 |
| 7 | R1 | 10.7 | 673 | 793 | 0.23 | 61.0 | 41.1 | 0.11 | 40,000 | 805 | 29.6 | 108 |
|  | R2 | 4.2 | 711 | 802 | 0.20 | 60.2 | 38.7 | 0.09 | 37,700 | 783 | 25.9 | 101 |
| 8 | R1 | 7.2 | 22,300 | 426,000 | 0.84 | 11.6 | 63.3 | 0.03 | 20,500 | 1,650 | 38.2 | 33 |
|  | R2 | 11.9 | 24,800 | 422,000 | 0.88 | 13.2 | 59.0 | 0.03 | 22,800 | 1,740 | 33.2 | 38 |
| 9 | R1 | 13.0 | 711 | 948 | 0.23 | 55.8 | 39.1 | 0.11 | 40,500 | 884 | 27.5 | 105 |
|  | R2 | 6.3 | 720 | 878 | 0.22 | 64.6 | 41.7 | 0.10 | 42,200 | 838 | 26.5 | 109 |
| 11 | R1 | 5.4 | 697 | 965 | 0.24 | 65.0 | 42.1 | 0.10 | 39,700 | 845 | 27.0 | 106 |
|  | R2 | 2.7 | 1,500 | 1,680 | 0.28 | 61.4 | 40.3 | 0.10 | 42,000 | 840 | 28.6 | 105 |
| 12 | R1 | 8.8 | 635 | 778 | 0.21 | 61.2 | 36.6 | 0.09 | 35,400 | 739 | 24.7 | 92 |
|  | R2 | 4.8 | 820 | 992 | 0.21 | 62.2 | 39.3 | 0.09 | 37,000 | 790 | 28.2 | 102 |
| 13 | R1 | 7.4 | 744 | 857 | 0.24 | 65.8 | 41.4 | 0.12 | 43,200 | 848 | 30.4 | 110 |
|  | R2 | 5.6 | 758 | 792 | 0.21 | 63.0 | 40.2 | 0.10 | 39,100 | 786 | 28.6 | 105 |
| 14 | R1 | 11.5 | 657 | 854 | 0.22 | 62.8 | 42.0 | 0.10 | 41,200 | 819 | 31.0 | 108 |
|  | R2 | 7.3 | 949 | 1,120 | 0.18 | 62.8 | 37.0 | 0.11 | 38,200 | 764 | 26.0 | 99 |
| 15 | R1 | 8.6 | 709 | 858 | 0.21 | 66.4 | 39.0 | 0.09 | 42,000 | 828 | 29.5 | 105 |
|  | R2 | 7.5 | 654 | 865 | 0.19 | 70.6 | 41.4 | 0.11 | 43,800 | 870 | 31.2 | 115 |
|  | Min | 2.7 | 635 | 778 | 0.18 | 11.6 | 36.1 | 0.03 | 20,500 | 739 | 24.7 | 33 |
|  | Max | 13.0 | 24,800 | 426,000 | 0.88 | 70.6 | 63.3 | 0.15 | 43,800 | 1,740 | 38.2 | 115 |
|  | Median | 7.0 | 735 | 885 | 0.23 | 62.9 | 40.6 | 0.10 | 39,600 | 839 | 27.7 | 105 |
|  | Mean | 7.0 | 2,607 | 33,556 | 0.27 | 59.5 | 41.7 | 0.10 | 38,269 | 893 | 28.3 | 99 |
|  | St Dev | 2.7 | 6,184 | 114,946 | 0.18 | 14.3 | 6.1 | 0.02 | 5,386 | 240 | 2.9 | 19 |
|  | %CV | 38 | 237 | 343 | 64 | 24 | 15 | 23 | 14 | 27 | 10 | 20 |

Table 5.2 Metal Concentration Summary Statistics Excluding Station 8: SDX-5 Post Drill Survey 2010 μg.g-1 dry sediment

|  | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Min | 2.7 | 635 | 778 | 0.18 | 54.9 | 36.1 | 0.09 | 34,600 | 739 | 24.7 | 89 |
| Max | 13.0 | 1,900 | 2,170 | 0.28 | 70.6 | 43.1 | 0.15 | 43,800 | 908 | 31.2 | 115 |
| Median | 6.6 | 725 | 876 | 0.22 | 63.4 | 40.3 | 0.10 | 39,850 | 833 | 27.5 | 105 |
| Mean | 6.8 | 862 | 1,019 | 0.22 | 63.5 | 40.1 | 0.10 | 39,654 | 826 | 27.7 | 104 |
| St Dev | 2.6 | 343 | 373 | 0.03 | 3.8 | 1.9 | 0.01 | 2,323 | 46 | 1.8 | 6 |
| %CV | 38 | 40 | 37 | 11 | 6 | 5 | 11 | 6 | 6 | 6 | 5 |

## Results

Initial examination of the replicate data indicates that replicate agreement was very good for all parameters at all stations.

Station 8 is distinctive, with very different characteristics to the other sample stations. Table 5.2 gives the summary statistics excluding the data from station 8. When the data is considered excluding station 8 the coefficient of variation between samples reduces to 5 & 6% for Cr, Cu, Fe, Mn, Pb and Zn, and 11% for Cd and Hg, indicating that there was very little variation at the remaining stations for these elements.

Replicate arsenic concentrations ranged from 2.7μg.g-1 at station 11 R2 to 13.0μg.g-1 at station 9 R1, the median and mean concentrations were 7.0μg.g-1 and the CV was moderate at 38%. The arsenic concentration at station 8 was within the range recorded at the other sample stations.

Ba extraction by nitric acid (HNO3) ranged from 635 to 1,900μg.g-1 at stations 12R1 and 3R1 respectively, with a median of 725μg.g-1 and mean of 862μg.g-1. The concentrations in samples from station 8 were far higher with 22,300 and 24,800μg.g-1.

Analysis for total barium (fusion) was carried out to identify the extent of contamination from drilling discharges as barite in drilling fluids interferes with the determination of HNO3 extracted Ba.

Excluding station 8 the concentration of total Ba ranged from 778μg.g-1 to 2,170μg.g-1 at stations 12R1 and 3R1 respectively, with median and mean concentrations of 876 and 1,019μg.g-1. The concentration of HNO3 Ba as a proportion of total Ba within these samples was generally high, ranging from 72 to 96%.

Replicate total Ba concentrations at station 8 were extremely high with 426,000 and 422,000μg.g-1. The proportion of HNO3 Ba in these samples was very low at 5 and 6% and indicates the presence of barite from discharged drilling fluid.

The median and mean values quoted for the following elements will exclude the data from station 8 and are provided in table 5.2.

The concentration of cadmium in replicate samples ranged from 0.18μg.g-1 at station 14R2 to 28μg.g-1 at station 11R2 with median and mean concentrations of 0.22μg.g-1. The replicate cadmium concentrations at station 8 were higher with 0.84 and 0.88μg.g-1.

Chromium concentrations range from 54.9 to 70.6μg.g-1 at stations 3R1 and 15R2 with median and mean concentrations of 63.4 and 63.5μg.g-1. The concentrations recorded at station 8 were lower with 11.6 and 13.2μg.g-1.

Replicate copper concentrations ranged from 36.2 to 43.1μg.g-1 at stations 3R1 and 6R1 with a median and mean concentration of 40.3 and 40.1μg.g-1. Higher concentrations of 63.3 and 59.0μg.g-1 were recorded at station 8.

Mercury concentrations ranged from 0.09μg.g-1 at stations 1R1, 7R2, 12R1, 12R2 and 15R1, to a maximum of 0.15μg.g-1 at station 2R2, with median and mean concentrations of 0.10μg.g-1. Concentrations recorded at station 8 were lower with 0.03μg.g-1 in both replicate samples.

The concentration of Iron in replicate samples ranged from 34,600 to 43,800μg.g-1 at stations 3R1 and 15R2 respectively with median and mean concentrations of 39,850 and 39654μg.g-1. Iron concentrations in samples from station 8 were lower with 20,500 and 22,800μg.g-1.

Manganese concentrations ranged from 739μg.g-1 at station 3R1 to 908μg.g-1 at station 2R1, with median and mean concentrations of 833 and 826μg.g-1. Higher concentrations of 1,650 and 1740μg.g-1 were observed at station 8.

Replicate lead concentrations ranged from 24.7 to 31.2μg.g-1 at stations 12R1 and 15R2 respectively, with median and mean concentrations of 27.5 and 27.7μg.g-1. The concentrations recorded at station 8 were slightly higher with 33.2 and 38.2μg.g-1.

Concentrations of Zinc in replicate samples ranged from 89μg.g-1 at station 3R1 to 115μg.g-1 at station 15R2. Lower concentration of 33 and 38μg.g-1 were observed at station 8.

Excluding the data from station 8, the minimum concentrations of Cr, Cu, Fe, Mn and Zn were all present in replicate 1 at station 3 and the highest concentrations of Cr, Fe, Pb and Zn were recorded in replicate 2 from station 15.

## Relationship between Metals

The relationship between elements was tested by a Pearson’s r correlation analysis of replicate values. Station 8 was omitted from the analysis as the sediment type and metal composition differs to all other stations.

The results of the correlation analysis are given in table 5.3 below. Moderate to high correlation coefficients have been given between elements Cr, Cu, Fe, Mn, Pb and Zn. Figure 5.1 gives the paired variable scatter plots, which indicate that the concentrations of each element are increasing together.

Moderate correlation coefficients of 0.56 and 0.55 were given between Cd and both extracted forms of Ba.

Table 5.3	Correlation between Replicate Metal Concentrations; SDX-5 Post Drill Survey 2010

|  | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| As | 1.00 |  |  |  |  |  |  |  |  |  |  |
| Ba | -0.19 | 1.00 |  |  |  |  |  |  |  |  |  |
| Ba Fusion | -0.14 | 0.99 | 1.00 |  |  |  |  |  |  |  |  |
| Cd | -0.06 | 0.56 | 0.55 | 1.00 |  |  |  |  |  |  |  |
| Cr | -0.16 | -0.34 | -0.35 | -0.02 | 1.00 |  |  |  |  |  |  |
| Cu | 0.00 | -0.24 | -0.23 | 0.37 | 0.69 | 1.00 |  |  |  |  |  |
| Hg | 0.02 | -0.07 | -0.06 | 0.30 | 0.27 | 0.40 | 1.00 |  |  |  |  |
| Fe | 0.13 | -0.27 | -0.26 | 0.14 | 0.61 | 0.70 | 0.29 | 1.00 |  |  |  |
| Mn | 0.04 | -0.22 | -0.20 | 0.29 | 0.59 | 0.76 | 0.33 | 0.73 | 1.00 |  |  |
| Pb | 0.31 | -0.21 | -0.20 | 0.11 | 0.48 | 0.63 | 0.25 | 0.76 | 0.45 | 1.00 |  |
| Zn | 0.04 | -0.47 | -0.46 | 0.07 | 0.63 | 0.81 | 0.36 | 0.85 | 0.72 | 0.73 | 1.00 |

Figure 5.1 Paired Variable Scatter Plots

## Comparison with Previous Survey Data

Table 5.4 below gives the averaged metal concentrations from the 2007 baseline survey and the 2010 post drill survey.

Other than a similar concentration of arsenic, the average concentration of all elements have changed between surveys at station 8. Along with the obvious increases in Ba concentrations, higher concentrations of Cd, Cu, Hg, Mn and Pb were recorded in 2010 whereas lower concentrations of Fe, Zn, and Cr were present. The characteristics at station 8 in 2007 were very similar to the other survey stations.

Slightly higher average Ba concentrations were also observed at stations 3 and 11 in 2010, with respective total Ba concentrations increasing from 734 and 749μg.g-1 to 2,075 and 1,322μg.g-1. Station 3 is located 250m SSE of the drill site and station 11 is 400m ENE of the drill site.

Overall there has been very little change in the concentration of metals between surveys. The universally higher concentrations of Hg and Zn recorded in 2010 (+20 & 30%) will be the result of analytical variation rather than an area wide increase in concentration.

Table 5.4a	Average Metal Concentrations µg.g-1 SDX-5 Baseline Survey 2007 & Post Drill Survey 2010

|  | As | Ba HNO3 | Ba Fusion | Cd | Cr | Cu |
| --- | --- | --- | --- | --- | --- | --- |
| Station | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 |
| 1 | 9.7 | 5.5 | 578 | 691 | 774 | 814 | 0.24 | 0.20 | 67.9 | 61.8 | 44.9 | 38.3 |
| 2 | 10.2 | 6.6 | 593 | 770 | 768 | 928 | 0.24 | 0.25 | 72.2 | 67.6 | 46.0 | 42.1 |
| 3 | 11.6 | 6.8 | 557 | 1,825 | 734 | 2,075 | 0.23 | 0.26 | 68.4 | 59.3 | 44.5 | 38.5 |
| 4 | 11.9 | 5.2 | 604 | 817 | 745 | 934 | 0.23 | 0.23 | 75.0 | 66.0 | 43.7 | 40.7 |
| 6 | 12.0 | 5.1 | 629 | 774 | 765 | 880 | 0.23 | 0.21 | 75.9 | 65.3 | 44.6 | 41.2 |
| 7 | 11.6 | 7.5 | 530 | 692 | 752 | 798 | 0.25 | 0.22 | 62.1 | 60.6 | 43.6 | 39.9 |
| 8 | 10.2 | 9.6 | 533 | 23,550 | 720 | 424,000 | 0.20 | 0.86 | 65.3 | 12.4 | 43.1 | 61.1 |
| 9 | 10.8 | 9.7 | 571 | 715 | 780 | 913 | 0.21 | 0.22 | 64.3 | 60.2 | 43.5 | 40.4 |
| 11 | 11.6 | 4.1 | 575 | 1,098 | 749 | 1,322 | 0.26 | 0.26 | 68.3 | 63.2 | 44.9 | 41.2 |
| 12 | 14.1 | 6.8 | 593 | 727 | 742 | 885 | 0.26 | 0.21 | 72.5 | 61.7 | 45.2 | 37.9 |
| 13 | 10.8 | 6.5 | 497 | 751 | 751 | 825 | 0.25 | 0.23 | 55.8 | 64.4 | 41.8 | 40.8 |
| 14 | 12.2 | 9.4 | 475 | 803 | 690 | 987 | 0.23 | 0.20 | 57.8 | 62.8 | 44.6 | 39.5 |
| 15 | 11.6 | 8.0 | 450 | 682 | 671 | 861 | 0.20 | 0.20 | 54.5 | 68.5 | 42.5 | 40.2 |
| min | 9.7 | 4.1 | 450 | 682 | 671 | 798 | 0.20 | 0.20 | 54.5 | 12.4 | 41.8 | 37.9 |
| max | 14.1 | 9.7 | 629 | 23,550 | 780 | 424,000 | 0.26 | 0.86 | 75.9 | 68.5 | 46.0 | 61.1 |
| median | 11.6 | 6.8 | 571 | 770 | 749 | 913 | 0.23 | 0.22 | 67.9 | 62.8 | 44.5 | 40.4 |
| mean | 11.4 | 7.0 | 553 | 2,607 | 742 | 33,556 | 0.23 | 0.27 | 66.1 | 59.5 | 44.1 | 41.7 |
| st dev | 1.1 | 1.8 | 53 | 6,300 | 32 | 117,314 | 0.02 | 0.18 | 7.0 | 14.4 | 1.2 | 6.0 |
| %CV | 10 | 26 | 10 | 242 | 4 | 350 | 9 | 65 | 11 | 24 | 3 | 14 |

Table 5.4b 	Average Metal Concentrations µg.g-1 SDX-5 Baseline Survey 2007 & Post Drill Survey 2010

|  | Fe | Hg | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- |
| Station | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 |
| 1 | 35,694 | 37,400 | 0.07 | 0.100 | 802 | 794 | 24.8 | 26.0 | 84.1 | 100.7 |
| 2 | 37,082 | 39,950 | 0.08 | 0.128 | 843 | 875 | 24.3 | 27.7 | 83.1 | 107.1 |
| 3 | 35,659 | 36,750 | 0.07 | 0.101 | 829 | 783 | 23.3 | 26.3 | 79.8 | 94.5 |
| 4 | 37,138 | 41,050 | 0.08 | 0.103 | 827 | 867 | 24.2 | 27.3 | 82.4 | 106.4 |
| 6 | 37,899 | 39,700 | 0.08 | 0.101 | 853 | 878 | 24.5 | 27.3 | 83.7 | 104.5 |
| 7 | 36,311 | 38,850 | 0.07 | 0.101 | 841 | 794 | 24.3 | 27.7 | 82.4 | 104.6 |
| 8 | 37,679 | 21,650 | 0.07 | 0.032 | 864 | 1695 | 24.5 | 35.7 | 82.2 | 35.5 |
| 9 | 37,562 | 41,350 | 0.08 | 0.102 | 815 | 861 | 25.2 | 27.0 | 85.7 | 107.0 |
| 11 | 35,260 | 40,850 | 0.08 | 0.101 | 784 | 843 | 25.1 | 27.8 | 86.9 | 105.4 |
| 12 | 40,832 | 36,200 | 0.08 | 0.092 | 909 | 764 | 25.3 | 26.5 | 87.6 | 97.3 |
| 13 | 37,825 | 41,150 | 0.07 | 0.108 | 840 | 817 | 23.5 | 29.5 | 78.0 | 107.7 |
| 14 | 36,645 | 39,700 | 0.07 | 0.103 | 835 | 792 | 24.4 | 28.5 | 81.1 | 103.3 |
| 15 | 37,676 | 42,900 | 0.07 | 0.100 | 856 | 849 | 23.7 | 30.3 | 78.0 | 109.7 |
| min | 35,260 | 21,650 | 0.07 | 0.03 | 784 | 764 | 23.3 | 26.0 | 78.0 | 35.5 |
| max | 40,832 | 42,900 | 0.08 | 0.13 | 909 | 1695 | 25.3 | 35.7 | 87.6 | 109.7 |
| median | 37,138 | 39,700 | 0.07 | 0.10 | 840 | 843 | 24.4 | 27.7 | 82.4 | 104.6 |
| mean | 37,174 | 38,269 | 0.08 | 0.10 | 838 | 893 | 24.4 | 28.3 | 82.7 | 98.8 |
| st dev | 1419 | 5357 | 0.00 | 0.02 | 31 | 244 | 0.6 | 2.5 | 3.0 | 19.5 |
| %CV | 4 | 14 | 6.32 | 21.79 | 4 | 27 | 3 | 9 | 4 | 20 |

Table 5.5 below gives the 2007 and 2009 metal concentrations at Shah Deniz Regional stations 31 and 32, which are located in a similar position and depth to the SDX-5 stations.

When the SDX-5 data is compared to the data from Regional stations 31 and 32, the only notable difference are the lower Cr concentrations in samples from SDX-5 stations, with concentrations ranging 55-70μg.g-1 (excluding station 8) compared to ≥85.9μg.g-1 at regional stations 31 and 32.

Table 5.5	Average 2007 & 2009 Metal Concentrations µg.g-1 at SD Regional Stations 31 & 32

|  | As | Ba HNO3 | Ba Fusion | Cd | Cr | Cu |
| --- | --- | --- | --- | --- | --- | --- |
| Station | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 |
| 31 | 18.4 | 15.4 | 699 | 805 | 1049 | 845 | 0.23 | 0.19 | 85.9 | 86.7 | 36.4 | 34.0 |
| 32 | 17 | 7.7 | 697 | 717 | 1037 | 770 | 0.16 | 0.16 | 87.3 | 88.8 | 40.2 | 35.0 |
|  | Fe | Hg | Mn | Pb | Zn |  |  |
| Station | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 | 2007 | 2009 |  |  |
| 31 | 38,300 | 41,900 | 0.10 | 0.09 | 733 | 912 | 21.6 | 26.5 | 86.4 | 99.1 |  |  |
| 32 | 39,800 | 40,500 | 0.10 | 0.10 | 785 | 810 | 23.6 | 28.1 | 91.9 | 102.3 |  |  |

## Metal Summary

The metal composition in replicate samples taken at station 8 differed to those taken from all other stations.

Excluding station 8 the variation between samples was very low and ranged from 5-11% for elements Cd, Cr, Cu, Hg, Fe, Mn, Pb and Zn. Variation between samples for both extracted forms of Ba and As were higher and ranged from 37-40%.

Excluding station 8, the presence of elements Cr, Cu, Fe, Mn, Pb and Zn were found to be interrelated, indicating that these metals were associated with the same mineral fraction of the sediment.

When the 2010 post drill data was compared to the results from the 2007 baseline survey, there was very little difference in metal concentrations. However, the results from station 8 indicate a large change in the metal composition between surveys, with the extremely high total Ba concentrations in 2010 indicating the presence of discharged drilling fluids. Slightly higher Ba concentrations were also recorded at stations 3 and 11, 250m SSE and 400m ENE of the drill site.