# Fieldwork and analytical programme

## Survey execution and sample collection

The survey was conducted between the 26th of July and the 2nd of August 2010, the sampling log is given in appendix 1. The survey vessel was the Svetlomor II, operated by OSCA.  The following personnel participated in the survey:

- James McNee, AmC Senior Consultant

- Ilgar Guliyev, AmC Senior Scientist

- Mustafa Gafarov, AmC Scientist

- Irada Israfilova, AmC Scientist

- Konul Guliyeva, AmC Scientist

- Faruhk Fursi, AmC Technician

- Kamran Ahmedov, AmC Technician

- Andrey Fomin, AmC Technician

- Valeh Karimov MENR Scientist

- Hikmet Zeynalov SOCAR Scientist

The 2010 survey sampled the same station positions as 2008. The layout of stations is given in figure 2.1.

Figure 2.1 2010 Survey Sample Stations

## Sampling & Analytical Programme

Details of the analytical methods are provided in Appendix 2 of this report.  The analytical work was conducted at AmC Caspian Environmental Laboratory. All sampling and laboratory work was carried out in accordance with AmC’s quality system.

A standard sediment survey was carried out, using a double 0.1 m2 Van Veen grab to collect samples from the top 10-15 cm of sediment.  Two replicate samples were collected at each station for physical (particle size) and chemical analysis and three replicate samples were collected for biological analysis (see table 2.1). Replicate independence was assured by processing one biology and one physical/chemistry sample from two of the three double grabs and a single biology sample from the third double grab. Sample station coordinates and the number of samples taken for each analysis is detailed in table 2.1.

Biological samples were washed on a 0.5 mm sieve, and all material retained was preserved in 4% formaldehyde solution. Subsamples for physical and chemical analysis were placed in appropriate labelled containers and stored in a freezer on the Svetlomor 2, then transferred to freezer storage at AmC’s Caspian Environmental Laboratory at the end of the survey. Sample station coordinates and the number of samples taken for each analysis is detailed in table 2.1.

Water samples were collected above and below the thermocline at stations 1, 6, 10 & 15 using a 12l Niskin Sampler, the water analysis plan is given in table 2.2.

Table 2.1	Sediment Sampling and Analysis Plan

|  |  |  |  | Physical and chemical analyses | Biological analysis |
| --- | --- | --- | --- | --- | --- |
| Station | Easting | Northing | Depth | HC1 | HM2 | PSA3 | Phenols4 | Taxonomy, abundance, and biomass |
| EAP 1001 | 538567 | 4432300 | 153 | 2 | 2 | 2 | 2 | 3 |
| EAP 1002 | 538112 | 4432066 | 153 | 2 | 2 | 2 | 2 | 3 |
| EAP 1003 | 538454 | 4432134 | 153 | 2 | 2 | 2 | 2 | 3 |
| EAP 1004 | 538725 | 4432167 | 152 | 2 | 2 | 2 | 2 | 3 |
| EAP 1005 | 538930 | 4432108 | 152 | 2 | 2 | 2 | 2 | 3 |
| EAP 1006 | 538054 | 4431886 | 163 | 2 | 2 | 2 | 2 | 3 |
| EAP 1007 | 538303 | 4431883 | 151 | 2 | 2 | 2 | 2 | 3 |
| EAP 1008 | 538550 | 4431740 | 150 | 2 | 2 | 2 | 2 | 3 |
| EAP 1009 | 538815 | 4432297 | 153 | 2 | 2 | 2 | 2 | 3 |
| EAP 1010 | 539061 | 4431883 | 152 | 2 | 2 | 2 | 2 | 3 |
| EAP 1011 | 538124 | 4431624 | 173 | 2 | 2 | 2 | 2 | 3 |
| EAP 1012 | 538416 | 4431681 | 150 | 2 | 2 | 2 | 2 | 3 |
| EAP 1013 | 538681 | 4431647 | 152 | 2 | 2 | 2 | 2 | 3 |
| EAP 1014 | 538931 | 4431669 | 152 | 2 | 2 | 2 | 2 | 3 |
| EAP 1015 | 538557 | 4431453 | 169 | 2 | 2 | 2 | 2 | 3 |
| EAP 1016 | 538053 | 4432752 | 157 | 2 | 2 | 2 | 2 | 3 |
| EAP 1017 | 539053 | 4432752 | 155 | 2 | 2 | 2 | 2 | 3 |
| EAP 1018 | 537553 | 4431886 | 214 | 2 | 2 | 2 | 2 | 3 |
| EAP 1019 | 539553 | 4431886 | 153 | 2 | 2 | 2 | 2 | 3 |

Table 2.1 (Continued)	Sediment Sampling and Analysis Plan

|  |  |  |  | Physical and chemical analyses | Biological analysis |
| --- | --- | --- | --- | --- | --- |
| Station | Easting | Northing | Depth | HC1 | HM2 | PSA3 | Phenols4 | Taxonomy, abundance, and biomass |
| EAP 1020 | 538053 | 4431020 | 202 | 2 | 2 | 2 | 2 | 3 |
| EAP 1021 | 539053 | 4431020 | 207 | 2 | 2 | 2 | 2 | 3 |

Projection TM: (Gauss Kruger Zn9N), Spheroid: Krassovsky 1940, Horizontal Datum: Pulkovo 1942 (AIOC97)

1	HC = Hydrocarbon analysis: THC by GC-FID, 2-6 ring PAH by GC-MS

2	HM = Heavy metal analysis: All metals except Hg analysed by ICP-OES, Hg analysed CVAFS

3	PSA = Particle size analysis: Grain size distribution, total organic matter (TOM), carbonate (CO3)

4	Phenols will be measured by spectrophotometry (Merck Spectroquant method)

Table 2.2 Water Sample Analysis Plan

| Determinand | Method | Method of sampling and preservation for transport to laboratory |
| --- | --- | --- |
| Temperature | pH meter | N/A – analyses conducted immediately |
| Salinity | Multimeter |  |
| Dissolved oxygen | DO meter |  |
| Turbidity | Turbidimeter |  |
| pH | pH meter |  |
| Total suspended solids (TSS) | EN 872 | Water is filtered through pre-weighed membrane filter. Filter is placed in labelled plastic Petri dish, dish is sealed and frozen. |
| Total nitrogen, total phosphorus, nitrate, nitrite, ammonia, phosphate, silicate, COD & BOD | Grasshoff et al | Water is poured into two (duplicate) sterile 1-litre plastic bottles, then frozen. 2 litres of water is sufficient for all nutrient analyses. |
| THC | GC-FID | Water is poured into 2 x 1litre, DCM-cleaned, amber glass bottle, then refrigerated |
| PAH | GC-MS |  |
| Phenols | Merck Spectroquant |  |
| Metals (Fe, Cd, Co, Cu, Ni, Pb & Zn) | ICP-MS | Water is poured from Niskin bottle into 0.5-L sterile plastic bottles, then refrigerated |