# Fieldwork and analytical programme

## Survey execution and sample collection

The survey was conducted from 6 - 7 August 2010, the sampling log is given in appendix 1 and the analytical methods are provided in appendix 2. The survey vessel was the Svetlomor II, operated by CBARS.  The following personnel participated in the survey:

- James McNee, AmC Senior Consultant

- Ilgar Guliyev, AmC Senior Scientist

- Mustafa Gafarov, AmC Scientist

- Irada Israfilova, AmC Scientist

- Konul Guliyeva, AmC Scientist

- Faruhk Fursi, AmC Technician

- Kamran Ahmedov, AmC Technician

- Andrey Fomin, AmC Technician

- Valeh Karimov MENR Scientist

- Hikmet Zeynalov SOCAR Scientist

## Sampling & Analytical Programme

## Sediment Samples

A standard sediment survey was carried out, using a double 0.1 m2 van Veen grab to collect samples from the top 10-15 cm of sediment. Two replicate samples were collected at each station for physical (particle size) and chemical analysis and three replicate samples were collected for biological analysis (see table 2.1). Replicate independence was assured by processing one biology and one physical/chemistry sample from two of the three double grabs and a single biology sample from the third double grab.

Biological samples were washed on a 0.5 mm sieve and all material retained was preserved in 4% formaldehyde solution. Subsamples for physical and chemical analysis were placed in appropriate labelled containers and stored in a freezer on the Svetlomor II, then transferred to freezer storage at AmC’s Caspian Environmental Laboratory at the end of the survey.

## Water Samples

Water samples were collected at stations 4, 7, 9 and 13 using a 12 L Niskin Sampler; the water analysis plan is given in table 2.2.  Two samples were taken at each station, one from surface waters (0-5m) and the second from below the thermocline, the depth of which was established using a submersible CTD sensor.

Table 2.1	Co-ordinates of Seabed Stations & Sampling Plan SDX-5 Post Drill Survey 2010

| Station | Water depth (m) | Easting (m) | Northing (m) | 1 | 2 | 3 | Biology |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | HC | HM | PSA |  | Water |
| 1 | 536 | 459699 | 4408489 | 2 | 2 | 2 | 3 |  |
| 2 | 536 | 459972 | 4408687 | 2 | 2 | 2 | 3 |  |
| 3 | 538 | 459725 | 4408688 | 2 | 2 | 2 | 3 |  |
| 4 | 538 | 459571 | 4408685 | 2 | 2 | 2 | 3 | 2 |
| 6 | 531 | 460098 | 4408903 | 2 | 2 | 2 | 3 |  |
| 7 | 534 | 459849 | 4408906 | 2 | 2 | 2 | 3 | 2 |
| 8 | 527 | 459625 | 4408903 | 2 | 2 | 2 | 3 |  |
| 9 | 528 | 459421 | 4408902 | 2 | 2 | 2 | 3 | 2 |
| 11 | 529 | 459971 | 4409121 | 2 | 2 | 2 | 3 |  |
| 12 | 527 | 459724 | 4409122 | 2 | 2 | 2 | 3 |  |
| 13 | 524 | 459472 | 4409121 | 2 | 2 | 2 | 3 | 2 |
| 14 | 525 | 459271 | 4409120 | 2 | 2 | 2 | 3 |  |
| 15 | 523 | 459596 | 4409335 | 2 | 2 | 2 | 3 |  |

- Hydrocarbon analysis: THC by GC-FID. 2-6 ring PAH by GC-MS. Phenols measured using spectrophotometry.

- Heavy metal analysis: Ba, Pb, Zn, Cu, Fe, Cr, Cd, As and Mn analysed by ICP-OES. Hg analysed by CVAFS.

- Particle size analysis: Grain size distribution, total organic matter (TOM) and carbonate (CO3).

Table 2.2	Water Sample Plan SDX-5 Post Drill Survey 2010

| Determinand | Method | Method of sampling and preservation for transport to laboratory |
| --- | --- | --- |
| Temperature | pH meter | N/A – analyses conducted immediately |
| Salinity | Multimeter |  |
| Dissolved oxygen | DO meter |  |
| Turbidity | Turbidimeter |  |
| pH | pH meter |  |
| Total suspended solids (TSS) | EN 872 | Water is filtered through pre-weighed membrane filter. Filter is placed in labelled plastic Petri dish, dish is sealed and frozen. |
| Total nitrogen, total phosphorus, nitrate, nitrite, ammonia, phosphate, silicate, COD & BOD | Grasshoff et al | Water is poured into two (duplicate) sterile 1-litre plastic bottles, then frozen. 2 litres of water is sufficient for all nutrient analyses. |
| THC | GC-FID | Water is poured into 2 x 1litre, DCM-cleaned, amber glass bottle, then refrigerated |
| PAH | GC-MS |  |
| Phenols | Merck Spectroquant |  |
| Metals Fe, Co, Ni, Cu, Zn, Cd & Pb) | ICP-MS | Water is poured from Niskin bottle into 0.5-L acid-washed, plastic bottles, acidified, then frozen |