# Seabed characteristics

## Results

The physical characteristics of the seabed were assessed from two replicate samples taken at each station. The 2010 replicate sediment properties are summarised in Table 3.1. PSA histograms are provided in Appendix 3.

Table 3.1	Replicate Physical Properties SDX-5 Post Drill Survey 2010

| Station Number | Rep | Mean diameter Xμm | Carbonate | Organic | Silt/Clay | Silt | Clay | Wentworth scale | Sorting index |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | % | % | % | % | % |  |  |
| 1 | 1 | 5 | 26 | 8.5 | 100 | 38 | 62 | Very fine silt | Good |
|  | 2 | 6 | 35 | 9.1 | 100 | 43 | 57 | Very fine silt | Good |
| 2 | 1 | 6 | 28 | 8.5 | 100 | 40 | 60 | Very fine silt | Good |
|  | 2 | 6 | 24 | 9.4 | 100 | 40 | 60 | Very fine silt | Good |
| 3 | 1 | 6 | 26 | 8.7 | 100 | 41 | 59 | Very fine silt | Good |
|  | 2 | 5 | 26 | 9.2 | 100 | 38 | 62 | Very fine silt | Good |
| 4 | 1 | 6 | 27 | 7.9 | 100 | 41 | 59 | Very fine silt | Good |
|  | 2 | 6 | 27 | 8.8 | 100 | 43 | 57 | Very fine silt | Good |
| 6 | 1 | 5 | 22 | 8.9 | 100 | 36 | 64 | Very fine silt | Good |
|  | 2 | 6 | 26 | 9.1 | 100 | 42 | 58 | Very fine silt | Good |
| 7 | 1 | 5 | 25 | 8.2 | 100 | 37 | 63 | Very fine silt | Good |
|  | 2 | 5 | 27 | 8.0 | 100 | 38 | 62 | Very fine silt | Good |
| 8 | 1 | 21 | 14 | 1.9 | 83 | 71 | 11 | Medium silt | Moderate |
|  | 2 | 26 | 14 | 1.9 | 82 | 74 | 7 | Medium silt | Poor |
| 9 | 1 | 5 | 26 | 9.1 | 100 | 38 | 62 | Very fine silt | Good |
|  | 2 | 6 | 23 | 11.1 | 100 | 40 | 60 | Very fine silt | Good |
| 11 | 1 | 6 | 26 | 8.9 | 100 | 46 | 54 | Very fine silt | Good |
|  | 2 | 6 | 25 | 12.2 | 100 | 41 | 59 | Very fine silt | Good |
| 12 | 1 | 6 | 24 | 7.4 | 100 | 43 | 57 | Very fine silt | Good |
|  | 2 | 6 | 27 | 8.3 | 100 | 41 | 59 | Very fine silt | Good |
| 13 | 1 | 5 | 26 | 8.1 | 100 | 39 | 61 | Very fine silt | Good |
|  | 2 | 7 | 26 | 8.6 | 100 | 55 | 45 | Very fine silt | Good |
| 14 | 1 | 6 | 25 | 8.1 | 100 | 42 | 58 | Very fine silt | Good |
|  | 2 | 6 | 25 | 9.0 | 100 | 40 | 60 | Very fine silt | Good |
| 15 | 1 | 6 | 26 | 8.7 | 100 | 40 | 60 | Very fine silt | Good |
|  | 2 | 6 | 25 | 9.1 | 100 | 40 | 60 | Very fine silt | Good |
|  | Min | 5 | 14 | 1.9 | 82 | 36 | 7 |  |  |
|  | Max | 26 | 35 | 12.2 | 100 | 74 | 64 |  |  |
|  | Median | 6 | 26 | 8.7 | 100 | 40 | 59 |  |  |
|  | Mean | 7 | 25 | 8.3 | 99 | 43 | 55 |  |  |
|  | St Dev | 5 | 4 | 2.1 | 5 | 9 | 14 |  |  |
|  | %CV | 70 | 16 | 25 | 5 | 22 | 25 |  |  |

Replicate agreement was very good at all stations. With the exception of station 8 adjacent to the well site, the physical properties were found to be very similar throughout, with well sorted very fine silt sediments with a mean diameter of 5-7μm and a silt-clay proportion of 100%. Carbonate and organic content ranged from 22-35% and 7.4-12.2% respectively.

Both replicates at station 8 had slightly coarser sediments with a mean diameter of 21 and 26μm and a lower silt-clay content of 83 and 82%. The proportion of silt in these samples was higher than all others with ~70% and the proportion of organic and carbonate content was lower with 1.9 and 14% respectively.

## Comparison with Previous Survey Data

Table 3.2 below gives the averaged sediment characteristics from the 2007 baseline survey and the 2010 post drill survey. The results indicate that the sediment structure has remained unchanged between 2007 and 2010 at all but station 8, with fine silt-clay sediment present throughout on both surveys.

The sediment structure at station 8 in 2007 was very similar to the other sample positions.  As noted the sediment is coarser in 2010 with a lower total silt-clay content, higher proportion of silt and a lower proportion of clay, carbonate and organic matter.

Table 3.2	Average Physical Properties SDX-5 Baseline Survey 2007 & Post Drill Survey 2010

| Station | Mean diameter μm | % Carbonate | % Organic | % Silt/Clay | % Silt | % Clay |
| --- | --- | --- | --- | --- | --- | --- |
|  | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 | 2007 | 2010 |
| 1 | 7 | 6 | 30 | 30 | 7 | 9 | 100 | 100 | 48 | 40 | 52 | 60 |
| 2 | 6 | 6 | 29 | 26 | 7 | 9 | 100 | 100 | 37 | 40 | 63 | 60 |
| 3 | 6 | 6 | 31 | 26 | 7 | 9 | 100 | 100 | 40 | 39 | 60 | 61 |
| 4 | 6 | 6 | 31 | 27 | 8 | 8 | 100 | 100 | 43 | 42 | 57 | 58 |
| 6 | 6 | 5 | 29 | 24 | 7 | 9 | 100 | 100 | 42 | 39 | 58 | 61 |
| 7 | 6 | 5 | 29 | 26 | 8 | 8 | 100 | 100 | 37 | 37 | 62 | 63 |
| 8 | 6 | 23 | 31 | 14 | 5 | 2 | 100 | 82 | 38 | 73 | 61 | 9 |
| 9 | 5 | 5 | 30 | 24 | 6 | 10 | 100 | 100 | 35 | 39 | 65 | 61 |
| 11 | 9 | 6 | 29 | 26 | 7 | 11 | 100 | 100 | 60 | 44 | 40 | 56 |
| 12 | 6 | 6 | 31 | 25 | 7 | 8 | 100 | 100 | 39 | 42 | 60 | 58 |
| 13 | 5 | 6 | 31 | 26 | 8 | 8 | 100 | 100 | 38 | 47 | 62 | 53 |
| 14 | 5 | 6 | 31 | 25 | 6 | 9 | 100 | 100 | 37 | 41 | 63 | 59 |
| 15 | 6 | 6 | 30 | 26 | 8 | 9 | 100 | 100 | 43 | 40 | 56 | 60 |

Table 3.3 below gives the sediment characteristics for stations 31 and 32 from the 2009 Shah Deniz Regional survey which are from a similar depth and position to the SDX-5 stations. When the data from these stations are compared to the SDX-5 data the results are very similar. Iindicating that the physical properties of the SDX-5 sediments are characteristic of sediments from this depth and location.

Table 3.3	Physical Properties of 2009 Shah Deniz Regional Survey Stations from Similar Depth & Location

| Station Number | Replicate | Mean diameter Xμm | Carbonate | Organic | Silt/Clay | Silt | Clay | Wentworth scale | Sorting index |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | % | % | % | % | % |  |  |
| 31 | 1 | 6 | 28 | 8.26 | 100 | 45 | 54 | Very fine silt | Good |
|  | 2 | 6 | 27 | 9.07 | 100 | 45 | 55 | Very fine silt | Good |
|  | 3 | 6 | 27 | 9.71 | 100 | 44 | 56 | Very fine silt | Good |
| 32 | 1 | 5 | 26 | 7.90 | 100 | 34 | 66 | Very fine silt | Good |
|  | 2 | 5 | 17 | 11.36 | 100 | 37 | 63 | Very fine silt | Good |
|  | 3 | 6 | 27 | 7.67 | 97 | 38 | 60 | Very fine silt | Good |

## Summary

In general the sediments around the SDX-5 well site were typical of the location and depth, with homogenous, well sorted, very fine silt with very little variation within and between stations. When compared to the baseline data from 2007, with the exception of station 8 where coarser sediments were present in 2010, there was no change in any of the sediment characteristics between years.

Station 8 is distinctive as the sediment from this position in 2010 had a higher mean particle size, lower total silt-clay content, higher proportion of silt and a lower proportion of clay, carbonate and organic matter. As the characteristics at this position in 2007 were very similar to the other sample stations this indicates that the sediment structure around station 8 has changed between 2007 and 2010.