# Metals in Sediments

## Results

Metal concentrations at each Central Azeri sample station were determined from 2 replicate sediment samples. Replicate values are given in Table 5.1. Tables 5.2 to 5.11 gives the range median and mean for each element recorded on previous Central Azeri surveys.  Figures 5.1 to 5.10 presents contour plots for each metal, for 2008 and 2010.

Table 5.1 Replicate Metal Concentrations Central Azeri Survey 2010 (μg.g-1)

| Station | Rep | Concentration of Metals |
| --- | --- | --- |
|  |  | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| CA 1001 | 1 | 14.3 | 4,654 | 6,133 | 1.05 | 51.6 | 24.7 | 0.086 | 28,688 | 461 | 17.8 | 62.6 |
|  | 2 | 9.5 | 4,732 | 5,449 | 0.97 | 39.9 | 20.3 | 0.179 | 24,882 | 385 | 13.8 | 50.5 |
| CA 1002 | 1 | 8.8 | 5,659 | 6,350 | 1.12 | 39.5 | 21.0 | 0.043 | 22,367 | 408 | 11.2 | 48.1 |
|  | 2 | 2.3 | 2,485 | 3,374 | 0.68 | 46.4 | 20.6 | 0.030 | 22,309 | 356 | 9.1 | 46.8 |
| CA 1003 | 1 | 13.0 | 3,632 | 4,649 | 0.85 | 35.7 | 20.3 | 0.042 | 21,275 | 360 | 11.7 | 44.2 |
|  | 2 | 17.8 | 14,082 | 14,549 | 1.50 | 58.6 | 28.7 | 0.076 | 26,888 | 549 | 23.9 | 68.4 |
| CA 1004 | 1 | 21.9 | 6,904 | 7,511 | 1.01 | 45.3 | 19.1 | 0.074 | 26,425 | 468 | 15.9 | 50.6 |
|  | 2 | 14.8 | 6,293 | 7,984 | 1.01 | 43.3 | 21.5 | 0.043 | 24,602 | 454 | 13.6 | 48.8 |
| CA 1005 | 1 | 1.6 | 2,984 | 3,537 | 0.82 | 61.8 | 24.9 | 0.034 | 28,864 | 401 | 11.3 | 63.9 |
|  | 2 | 9.9 | 4,391 | 5,347 | 1.01 | 53.6 | 23.3 | 0.048 | 28,776 | 414 | 14.3 | 60.7 |
| CA 1006 | 1 | 17.0 | 11,266 | 37,039 | 1.94 | 54.5 | 33.6 | 0.065 | 26,402 | 518 | 27.0 | 66.3 |
|  | 2 | 16.1 | 9,693 | 14,473 | 1.40 | 37.5 | 17.9 | 0.042 | 22,842 | 357 | 17.0 | 46.5 |
| CA 1008 | 1 | 10.9 | 4,243 | 5,246 | 0.67 | 57.6 | 27.2 | 0.161 | 26,567 | 553 | 12.7 | 64.4 |
|  | 2 | 17.8 | 2,666 | 3,547 | 0.41 | 62.5 | 26.7 | 0.081 | 34,170 | 484 | 11.3 | 73.4 |
| CA 1009 | 1 | 12.7 | 21,851 | 30,814 | 2.13 | 40.9 | 26.4 | 0.118 | 25,148 | 365 | 22.9 | 84.6 |
|  | 2 | 7.2 | 6,364 | 8,853 | 1.10 | 44.3 | 26.4 | 0.070 | 21,985 | 357 | 14.0 | 55.6 |
| CA 1010 | 1 | 12.8 | 3,756 | 5,931 | 0.52 | 36.9 | 12.3 | 0.095 | 24,093 | 337 | 12.2 | 44.4 |
|  | 2 | 19.2 | 3,773 | 4,713 | 0.70 | 33.6 | 9.9 | 0.087 | 22,387 | 326 | 12.7 | 39.9 |
| CA 1011 | 1 | 4.2 | 5,089 | 7,160 | 0.20 | 39.2 | 20.5 | 0.112 | 22,550 | 428 | 13.3 | 46.2 |
|  | 2 | 5.5 | 2,869 | 4,565 | 0.52 | 56.1 | 27.5 | 0.100 | 25,654 | 445 | 9.5 | 59.3 |
| CA 1012 | 1 | 13.8 | 5,792 | 7,252 | 0.43 | 36.6 | 21.0 | 0.041 | 21,606 | 380 | 13.0 | 46.5 |
|  | 2 | 21.0 | 3,797 | 4,683 | 0.83 | 35.7 | 19.2 | 0.030 | 21,758 | 333 | 12.2 | 41.7 |
| CA 1013 | 1 | 18.7 | 3,914 | 5,828 | 0.85 | 42.5 | 22.3 | 0.046 | 23,682 | 390 | 13.2 | 52.0 |
|  | 2 | 13.5 | 4,443 | 6,271 | 0.73 | 37.1 | 17.6 | 0.028 | 23,031 | 377 | 14.7 | 49.2 |
| CA 1014 | 1 | 11.4 | 4,980 | 6,700 | 0.67 | 62.2 | 27.3 | 0.025 | 28,562 | 428 | 14.5 | 66.5 |
|  | 2 | 17.4 | 2,973 | 4,783 | 0.26 | 50.4 | 21.7 | 0.049 | 24,269 | 377 | 9.6 | 53.6 |
| CA 1015 | 1 | 10.7 | 23,245 | 35,565 | 2.52 | 48.3 | 28.7 | 0.040 | 24,116 | 410 | 24.2 | 59.0 |
|  | 2 | 7.8 | 25,037 | 45,636 | 2.34 | 40.0 | 25.1 | 0.035 | 22,911 | 386 | 26.5 | 59.5 |

Table 5.1 Replicate Metal Concentrations Central Azeri Survey 2010 (μg.g-1)

| Station | Rep | Concentration of Metals |
| --- | --- | --- |
|  |  | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| CA 1016 | 1 | 10.8 | 7,805 | 13,224 | 1.27 | 51.7 | 28.5 | 0.039 | 27,926 | 384 | 17.0 | 62.8 |
|  | 2 | 22.3 | 8,210 | 14,289 | 0.40 | 35.6 | 22.5 | 0.036 | 22,758 | 342 | 16.3 | 49.8 |
| CA 1017 | 1 | 17.8 | 6,056 | 6,236 | 0.47 | 50.6 | 24.3 | 0.027 | 27,476 | 409 | 13.6 | 56.0 |
|  | 2 | 12.6 | 8,900 | 10,842 | 0.85 | 51.8 | 22.9 | 0.027 | 25,514 | 414 | 15.8 | 56.1 |
| CA 1018 | 1 | 3.7 | 5,516 | 7,424 | 0.75 | 35.4 | 17.5 | 0.035 | 19,828 | 368 | 10.7 | 42.6 |
|  | 2 | 15.0 | 9,955 | 15,092 | 0.57 | 35.3 | 17.3 | 0.047 | 19,694 | 359 | 13.3 | 44.5 |
| CA 1019 | 1 | 14.8 | 4,743 | 6,633 | 0.86 | 42.7 | 20.8 | 0.030 | 22,086 | 363 | 13.0 | 45.5 |
|  | 2 | 10.5 | 5,738 | 8,595 | 1.11 | 34.3 | 13.6 | 0.026 | 19,754 | 342 | 11.2 | 39.5 |
| CA 1020 | 1 | 5.2 | 4,200 | 5,236 | 1.23 | 34.2 | 18.4 | 0.031 | 20,123 | 348 | 8.7 | 39.6 |
|  | 2 | 10.6 | 2,964 | 3,922 | 0.38 | 48.1 | 21.5 | 0.039 | 25,365 | 385 | 13.4 | 142.4 |
| CA 1021 | 1 | 37.9 | 2,470 | 3,401 | 0.41 | 62.2 | 26.4 | 0.030 | 42,285 | 768 | 14.3 | 64.4 |
|  | 2 | 8.3 | 3,415 | 4,418 | 0.52 | 57.9 | 29.6 | 0.031 | 28,084 | 481 | 11.9 | 58.9 |
| CA 1022 | 1 | 17.6 | 7,974 | 10,503 | 0.53 | 49.4 | 27.3 | 0.077 | 26,008 | 503 | 15.5 | 61.4 |
|  | 2 | 16.1 | 5,244 | 7,710 | 0.92 | 39.8 | 19.5 | 0.061 | 23,931 | 390 | 14.6 | 45.8 |
| Minimum |  | 1.6 | 2470 | 3374 | 0.20 | 33.6 | 9.9 | 0.02 | 19694 | 326 | 8.7 | 39.5 |
| Maximum |  | 37.9 | 25037 | 45636 | 2.52 | 62.5 | 33.6 | 0.18 | 42285 | 768 | 27.0 | 142.4 |
| Median |  | 12.9 | 5035 | 6491 | 0.84 | 43.8 | 22.0 | 0.04 | 24192 | 388 | 13.5 | 52.8 |
| Average |  | 13.2 | 6780 | 10035 | 0.92 | 45.7 | 22.5 | 0.06 | 24944 | 413 | 14.6 | 56.3 |
| Standard Deviation |  | 6.54 | 5304 | 9635 | 0.53 | 9.15 | 4.89 | 0.04 | 4085 | 80.46 | 4.40 | 16.95 |
| CV |  | 50% | 78% | 96% | 58% | 20% | 22% | 62% | 16% | 19% | 30% | 30% |

Overall, replicate agreement was moderate to good for most elements at 19 of the 21 stations, with poor agreement only at stations 3 and 9.  The most consistent between-replicate differences were observed for barium, lead, arsenic and iron.

### Arsenic

Replicate arsenic concentrations ranged from 1,6 μg.g-1 at station 5R1 to 37.9 8 μg.g-1 at station 21R1. The median and mean concentrations were 13.2 and 12.9 μg.g-1 respectively and variation between samples was moderate with a CV of 50%.  At stations where high arsenic concentrations were observed, this was associated with only one replicate; in each case, concentrations in the corresponding replicate were low.  Figure 5.1 shows that the pattern of distribution differs between 2008 and 2010, although both surveys feature higher concentrations around stations 4 and 21.

Figure 5.1  Comparison of spatial patterns in arsenic concentration, 2008 and 2010

Table  5.2 summarises the range, mean and coefficient of variation in arsenic concentrations over the series of surveys between 1998 and 2010.  There has been no distinctive trend since 2004.  This, together with the evidence from Figure 5.1 that spatial patterns are patchy and of limited consistency, suggests that there have been no systematic changes over time, and that arsenic concentrations are not observably influenced by platform operations.

Table 5.2  Overall trends in arsenic concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 1.6 | 13.2 | 37.9 | 50 |
| 2008 | 5.1 | 9.9 | 34.8 | 55 |
| 2006 | 4.1 | 11.2 | 27.8 | 50 |
| 2004 | 5.0 | 11.4 | 32.8 | 55 |
| 2001 | 2.0 | 6.0 | 15.0 | 64 |
| 1998 | Not measured |

### Barium

Analysis for total barium (fusion) was carried out to identify the extent of contamination from drilling discharges as barite in drilling fluids interferes with the determination of HNO3 extracted Ba. In general HNO3 extracted Ba as a % of total Ba was high, averaging 74%.

Replicate Ba fusion concentrations ranged from 3374 μg.g-1 to 45636 μg.g-1. The respective median and mean concentrations were 6,491 and 10035 μg.g-1 and the CV was high at 96%.

Replicate HNO3 extracted Ba ranged from 2470 μg.g-1 to 25037 μg.g-1. The median and mean concentrations were 5035 and 6780 respectively and the %CV of 78 indicates a large variation between samples.

For both forms of Ba, Figure 5.2 indicates the presence of a distinct footprint around the platform, with the highest concentrations, in both 2008 and 2010, extending to the NW and SE of the platform.  A notable difference between the surveys is that concentrations are lower in 2010 at station 17.  However, a common feature is that in both surveys concentrations are high at stations 6, 9 and 15,

Figure 5.2  Comparison of spatial patterns in barium concentration, 2008 and 2010

Table 5.3  Overall trends in barium concentrations, 1998-2010

|  | Ba HNO3 | Ba Total |
| --- | --- | --- |
|  | Min | Mean | Max | CV | Min | Mean | Max | CV |
| 2010 | 2470 | 6780 | 25037 | 78 | 3374 | 10035 | 45636 | 96 |
| 2008 | 900 | 6339 | 19000 | 71 | 1250 | 8584 | 26600 | 79 |
| 2006 | 1030 | 9200 | 24800 | 69 | 1100 | 10651 | 29300 | 68 |
| 2004 | 1165 | 6424 | 23607 | 83 | 1430 | 9829 | 33300 | 82 |
| 2001 | 2993 | 6956 | 9678 | 24 | Not measured |

Table 5.3 (Cont) Overall trends in barium concentrations, 1998-2010

|  | Ba HNO3 | Ba Total |
| --- | --- | --- |
|  | Min | Mean | Max | CV | Min | Mean | Max | CV |
| 1998 | 1450 | 2183 | 2760 | 24 | Not measured |

Table 5.3 summarises the trends in coefficient of variation and in minimum, mean and maximum concentrations over time.  Whilst there has been no consistent trend in minimum or mean values, it is clear that maximum concentrations increased markedly between 2001 (baseline survey) and 2004 (first post-operational survey), and remained high thereafter.  An equally marked increase in variability coincided with the increase in maximum concentrations, reflecting the effect of barite deposition following the discharge of water-based mud on cuttings during drilling operations.  There is, however, no evidence of any progressive increase in maximum concentrations between 2004 and 2010, indicating that the barite footprint is both restricted and stable.

### Cadmium

Cadmium concentrations ranged from 0.2 to 2.52 μg.g-1, with median and mean values of 0.84 and 0.92 μg.g-1.  The coefficient of variation was 58%, indicating that variation was higher than would be expected on the basis of normal sampling and analytical uncertainty.  As with barium, the distribution of concentrations indicated a patch of higher levels around the platform at stations 6, 9, and 15.

Figure 5.3 Comparison of spatial patterns in cadmium concentration, 2008 and 2010

Table 5.4  Overall trends in cadmium concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 0.2 | 0.92 | 2.52 | 58 |
| 2008 | 0.13 | 0.36 | 0.75 | 39 |
| 2006 | 0.07 | 0.43 | 0.87 | 43 |
| 2004 | 0.1 | 0.17 | 0.24 | 21 |
| 2001 | 0.24 | 0.54 | 0.73 | 28 |
| 1998 | 0.19 | 0.23 | 0.26 | 9 |

Table 5.4 summarises the trends in CV, minimum, mean and maximum cadmium concentrations over time.  Between 1998 and 2008 there was no systematic trend in concentration; the highest mean value for this period was recorded in the 2001 baseline survey.  However, the coefficient of variation increased over this period from 9% to around 40%.  In 2010, the minimum, mean and maximum concentrations were all substantially higher than in 2008, and the coefficient of variation was also substantially higher.  This indicates, when considered together with Figure 5.3, that concentrations at stations close to the platform have increased over the past two years.

### Chromium

Chromium concentrations ranged from 33 to 62 μg.g-1, with median and mean values of 43.8 and 45.7 μg.g-1. The coefficient of variation was 20%, suggesting that there was little systematic variation.  Figure 5.4 shows that the distribution of values differed between 2008 and 2010, with relatively high concentrations at stations 14 and 21 a common feature.  The apparently high concentration at station 22 in 2008 reflected a high value in one replicate only; the 2010 results are similar to those for the second replicate at that station, and suggest that the differences are a result of natural sampling variability.

Figure 5.4  Comparison of spatial patterns in chromium concentration, 2008 and 2010

Table 5.5 summarises the CV and minimum, mean and maximum concentrations observed in surveys between 1998 and 2010.  Coefficients of variation have remained low, and relatively stable, between 2001 and 2010.  Whilst minimum concentrations have also been quite constant over the majority of the surveys,  mean concentrations were around 30 μg.g-1(+/- 5) in the 1998-2004 surveys, then rose to about 45 μg.g-1 (+/- 5) in 2006-2010.  The trend for maximum concentrations is different, with a steady increase from about 40 μg.g_1 in 1998 to 80 ug-1 in 2008.  Maximum concentration in 2010 was somewhat lower, at 62 μg.g-1.  Given the low coefficients of variation within surveys, the large fluctuations in concentration between surveys are difficult to account for.  The spatial patterns do not indicate an association with platform operations.

Table 5.5  Overall trends in chromium concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 33.6 | 45.7 | 62.5 | 20 |
| 2008 | 32.1 | 48 | 80.9 | 21 |
| 2006 | 26.3 | 40.6 | 66.2 | 25 |
| 2004 | 22.5 | 34.4 | 51 | 19 |
| 2001 | 18.9 | 27.1 | 41.9 | 19 |
| 1998 | 29.6 | 34.9 | 41.1 | 9 |

### Copper

Copper concentrations ranged from 9.9 to 33.6 μg.g-1, with median and mean values of 22 and 22.5 μg.g-1.  The coefficient of variation was 22%, suggesting that there was little systematic variation.  Figure 5.5 illustrates the spatial distribution of concentrations in 2008 and 2010. While these show some similarities in overall pattern, there is no clear match from year to year with respect to the location of the highest concentrations.  In 2010, the highest concentrations appear to be at stations close to the platform, but also at station 21, at the southern edge of the survey area.

Table 5.6 summarises trends in the coefficient of variation, and minimum, mean and maximum concentrations between 1998 and 2010. Coefficients of variation have been low in all surveys, indicating an absence of systematic variation.  There has been no marked overall trend in minimum, mean or maximum concentration between 2006 and 2010.

Figure 5.5  Comparison of spatial patterns in copper concentration, 2008 and 2010

Table 5.6  Overall trends in copper concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 9.9 | 22.5 | 33.6 | 22 |
| 2008 | 14 | 22.9 | 34 | 19 |
| 2006 | 10.1 | 21.3 | 33.9 | 24 |
| 2004 | 8.8 | 19.1 | 35.2 | 36 |
| 2001 | 13.7 | 18 | 20.9 | 11 |
| 1998 | 19.8 | 24.7 | 30.3 | 13 |

### Mercury

Mercury concentrations ranged from 0.02 to 0.18 μg.g-1, with a median and mean of 0.04 and 0.06 μg.g-1.  The coefficient of variation of 62% was sufficiently high to indicate real variation across the survey area.

Figure 5.6 illustrates the spatial distribution of concentrations in 2008 and 2010.  The patterns are quite different in some respects. Of the stations with relatively high concentrations in 2008 (1, 6, 12, 17), only one (station 1) also has relatively high concentration in 2010.  In contrast, some stations at which relatively low concentrations were observed in 2008 (10, 11, 8, 9) had relatively high concentrations in 2010.

Table 5.7 summarises the CV and minimum, mean, and maximum concentrations in each survey between 1998 and 2010.  Coefficients of variation were low in the 1998 and 2001 baseline surveys (20%), increased to 30-40% in the 2004-2008 surveys, and increased again to 62% in the 2010 survey.  No clear trend is apparent, however, in the concentration parameters; whilst the 2008 values are similar to the baseline values, much higher values (3-5 times baseline levels) occur in the 2004 and 2010 surveys.

Figure 5.6  Comparison of spatial patterns in mercury concentration, 2008 and 2010

Table 5.7  Overall trends in mercury concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 0.02 | 0.06 | 0.18 | 62 |
| 2008 | 0.016 | 0.036 | 0.063 | 32 |
| 2006 | 0.015 | 0.036 | 0.082 | 40 |
| 2004 | 0.05 | 0.13 | 0.28 | 41 |
| 2001 | 0.019 | 0.03 | 0.041 | 20 |
| 1998 | 0.04 | 0.05 | 0.06 | 20 |

### Iron

Iron concentrations ranged from 19694 go 42285 μg.g-1, with median and average values of 24192 and 24944 μg.g-1 respectively.  The coefficient of variation was low (16%), suggesting that there was little systematic variation over the survey area.  The highest concentrations were observed at station 21, at the southern edge of the survey area (Figure 5.7), with the next highest concentrations located around stations 14 and 17 (SW of the platform) and 5 and 8 (NE of the platform).  The pattern of distribution did not correspond closely to that observed in 2008, and in neither survey did the pattern appear to be related to the platform location.

Figure 5.7  Comparison of spatial patterns in iron concentration, 2008 and 2010

Table 5.8 summarises trends the minimum, average, and maximum iron concentrations, and the corresponding coefficients of variation, for all surveys conducted at the CA location between 1998 and 2010. Coefficients of variation were low in all surveys. There does, however, seem to have been an increase in minimum, average and maximum concentration, with the most marked change occurring between the 2004 and 2006 surveys.  Examination of Table 5.13 (which presents average station data for 2004-2010) indicates that the changes shown in Table 5.8 occurred at all stations within the survey area.

Table 5.8  Overall trends in iron concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 19694 | 24944 | 42285 | 16 |
| 2008 | 20500 | 27029 | 41700 | 16 |
| 2006 | 19100 | 25698 | 36100 | 17 |
| 2004 | 14751 | 19229 | 28094 | 14 |
| 2001 | 11496 | 14471 | 21345 | 17 |
| 1998 | 16310 | 19104 | 22060 | 10 |

### Manganese

Manganese concentrations ranged from 326 to 768 μg.g-1, with median and mean concentrations of 377 and 413 μg.g-1.  The coefficient of variation was low, indicating that the range and distribution of values did not represent systematic variation.  This is confirmed in Figure 5.8, which shows that in both the 2008 and 2010 surveys, the concentration of manganese at station 21 was considerably higher than at other stations, and that with this exception the range of values was small.  Some differences are apparent between 2008 and 2010; in particular, concentrations at stations 4, 14 and 17 were relatively higher in the earlier survey.

Figure 5.8  Comparison of spatial patterns in manganese concentration, 2008 and 2010

Table 5.9 summarises trends in the minimum, mean and maximum concentrations of manganese over three surveys between 2006 and 2010. The differences between surveys are small, and do not indicate any real trends. Coefficients of variation were below 20% in the most recent two surveys, indicating that there was little real variation across the survey area.

Table 5.9  Overall trends in manganese concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 326 | 413 | 768 | 19 |
| 2008 | 323 | 411 | 554 | 13 |
| 2006 | 291 | 384 | 724 | 24 |
| 2004 | Not measured |
| 2001 | Not measured |
| 1998 | Not measured |

### Lead

Lead concentrations ranged from 8.7 tp 27 μg.g-1, with median and average concentrations of 13.5 and 14.6 μg.g-1. The coefficient of variation was moderate,  at 30%, indicating the possibility of systematic variation.  Figure 5.9 shows that in both 2008 and 2010, the pattern of distribution of lead concentrations does indeed appear systematic, with concentration contours which are spatially related to the platform location.  In both surveys, these patterns also closely matched the pattern of distribution of barium concentrations.  This is particularly striking, since there appears to have been a change in these patterns, with the apparent ‘footprint’ shifting from an ellipse oriented to the SW of the platform to an ellipse oriented to the NW of the platform.

Figure 5.9  Comparison of spatial patterns in lead concentration, 2008 and 2010

Table 5.10 summarises trends in the minimum, mean and maximum concentrations, and in the coefficient of variation, observed over 6 surveys.  Interestingly, in relation to the apparent patterns in Figure 5.9, the table shows that there has been a progressive overall decrease in concentration since 1998, accompanied by a substantial increase in coefficient of variation following commencement of platform operations.

Table 5.10  Overall trends in lead concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 8.7 | 14.6 | 27.0 | 30 |
| 2008 | 13.1 | 19.3 | 30.0 | 21 |
| 2006 | 12.0 | 16.9 | 29.6 | 23 |
| 2004 | 6.2 | 16.0 | 31.4 | 36 |
| 2001 | 12.8 | 18.8 | 23.2 | 16 |
| 1998 | 25.5 | 30.0 | 33.0 | 9 |

### Zinc

Zinc concentrations ranged for 39.5 to 142.4 μg.g-1, with median and mean concentrations of 52.8 and 56.3 μg.g-1.  Figure 5.10 show that the pattern of relative concentrations differed between 2008 and 2010; stations with the highest concentrations in 2008 were not those with the highest concentrations in 2010, and the relative difference at station 20 is particularly striking.  In 2010, the high average concentration at station 20 was due to a single replicate.  With the exception of this replicate, the highest concentration was substantially less at 84.6 μg.g-1.  Average concentrations were slightly elevated at stations 8 and 9, to the immediate NE of the platform.

Figure 5.10 Comparison of spatial patterns in zinc concentration, 2008 and 2010

Table 5.11 summarises the trends in minimum, mean and maximum concentrations, and in coefficient of variation, over 6 surveys between 1998 and 2010.  Coefficients of variation were very low between 1998 and 2008, but increased to 30% in the 2010 survey.  Minimum and mean concentrations have fluctuated considerably between surveys, but show no overall trend.

Table 5.11  Overall trends in zinc concentrations, 1998-2010

|  | Min | Mean | Max | CV |
| --- | --- | --- | --- | --- |
| 2010 | 39.5 | 56.3 | 142.4 | 30 |
| 2008 | 45.9 | 61.9 | 61.8 | 12 |
| 2006 | 32.4 | 49.6 | 72.8 | 18 |
| 2004 | 36.9 | 50.8 | 73.1 | 14 |
| 2001 | 32.0 | 39.6 | 52.9 | 14 |
| 1998 | 52.5 | 59.7 | 69.0 | 8 |

## Relationship between Metals

The relationship between elements was examined by a correlation analysis of replicate values (Table 5.2). This provides only an approximate indication of the presence of linear relationships, and is of limited value in instances where data are grouped or clustered. The majority of ‘moderate’ correlation coefficients (involving iron, copper, chromium, manganese and zinc) reflect natural variation in the mineral-derived fractions of the sediment (silt, clay and fine sand), overlaid with the influence of elements present in shell fragments.

The most notable, and apparently strongest, associations were between barium, cadmium and lead.

Paired variable plots (Figure 5.3) for these three metals do confirm a positive association, but the plots show clearly that the relationships are strongly influenced by a small number of high values, and that the majority of values lie in clusters within which the relationship is much less distinct.  In each case, the high values are associated with stations 6, 9 and 15, suggesting that the chemical composition of sediments at these stations is in some respects distinct from that at the remaining stations.

Figure 5.3  Paired variable plots for Cd, Ba (fusion) and Pb

Table 5.12 Correlation between Replicate Metal Concentrations, Central Azeri Survey 2010

|  | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| As | 1.00 |  |  |  |  |  |  |  |  |  |  |
| Ba | -0.03 | 1.00 |  |  |  |  |  |  |  |  |  |
| Ba Fusion | -0.02 | 0.93 | 1.00 |  |  |  |  |  |  |  |  |
| Cd | -0.14 | 0.83 | 0.83 | 1.00 |  |  |  |  |  |  |  |
| Cr | 0.09 | -0.10 | -0.07 | -0.08 | 1.00 |  |  |  |  |  |  |
| Cu | 0.01 | 0.31 | 0.37 | 0.29 | 0.76 | 1.00 |  |  |  |  |  |
| Hg | -0.08 | 0.02 | -0.01 | 0.00 | 0.05 | 0.07 | 1.00 |  |  |  |  |
| Fe | 0.47 | -0.14 | -0.12 | -0.14 | 0.80 | 0.53 | 0.07 | 1.00 |  |  |  |
| Mn | 0.48 | -0.04 | -0.01 | -0.07 | 0.70 | 0.57 | 0.16 | 0.81 | 1.00 |  |  |
| Pb | 0.19 | 0.84 | 0.88 | 0.77 | 0.13 | 0.48 | 0.08 | 0.13 | 0.22 | 1.00 |  |
| Zn | 0.01 | 0.13 | 0.13 | 0.05 | 0.48 | 0.46 | 0.09 | 0.41 | 0.27 | 0.27 | 1.00 |

## Trends in average values by station

Station-by-station comparisons can only be made on the basis of average station values, and are constrained by the fact that a number of stations have been relocated in successive surveys in order to avoid seabed infrastructure.  However, examination of these data can still assist in interpretation, by providing the basis for the contour diagrams in section 5.1 and by indicating the extent to which changes are survey-wide or are associated with particular stations.  Table 5.14 collates average concentrations of elements for four surveys between 2004 and 2010 (ie, over the period during which the Central Azeri platform has been operational).

Table 5.13 provides a qualitative summary of the trends present in Table 5.14, taking into account the underlying coefficients of variation.

Table 5.13  Narrative summary of main trends in metal concentration

| Element | Summary |
| --- | --- |
| Arsenic | No systematic station-by-station trends at 12 stations. Increases of up to 50% at stations 3, 4, 10, 12, 13, 14 and 17 between 2008 and 2010, but overall changes since 2004 not so marked. Increases are spread across survey area, with no spatial link to the platform location. |
| Barium (fusion) | No systematic change at 13 stations, with a decrease observed at 3 stations. Marked increases observed 2008-2010 at stations 9 and 15, whilst concentrations at station 6 have remained consistently high over all four surveys |
| Cadmium | Large increases (3-5 fold) at 17 stations between 2008 and 2010. Overall increase at all stations. Increase observed across survey area between 2004 and 2006, with little change between 2006 and 2008. |
| Chromium | Increased concentration at 3 stations, decrease at 6 stations, between 2008 and 2010. Changes relatively small, and no real change observed at the majority of stations. No evidence of meaningful trends, either spatially or over time. |
| Copper | Increase at one station, decrease at two stations between 2008 and 2010. No real change at other stations, and no evidence of meaningful trends in space or time |
| Iron | Little overall change between 2008 and 2010. A 30-50% increase across the survey area was observed between 2004 and 2006, but no meaningful trends since 2006 |
| Mercury | Increased concentrations (3-4 fold) at 9 stations (1, 3, 4, 5, 6, 8, 9, 10, 11) between 2008 and 2010, little change at other stations. An overall decrease was observed between 2004 and 2006, with little change between 2006 and 2008. Overall, between 2004 and 2010 there has been a net decrease in concentration at all but one station. |
| Manganese | Little change over time across the survey area |
| Lead | Decrease in concentration at 11 stations between 2008 and 2010. little net change at remaining stations. Little overall trend between 2004 and 2010. |
| Zinc | Increase at two stations, decrease at 8 stations, between 2008 and 2010. No clear overall spatial or temporal trends |

Table 5.14 Comparison of Average Metal Concentrations, Central Azeri Surveys 2004, 2006, 2008 and 2010  (μg.g-1)

|  | As | Ba HNO3 | Ba Fusion |
| --- | --- | --- | --- |
|  | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 |
| St 1 | 9.3 | 10.1 | 9.8 | 11.9 | 3219 | 5635 | 3715 | 4693 | 3885 | 7690 | 4640 | 5791 |
| St 2 | 5.1 | 6.7 | 5.2 | 5.5 | 2167 | 6095 | 3480 | 4072 | 2555 | 7740 | 5745 | 4862 |
| St 3 | 7.1 | 12.1 | 8.3 | 15.4 | 6082 | 5130 | 4270 | 8857 | 7935 | 5505 | 6150 | 9599 |
| St 4 | 15.1 | 7.2 | 21.2 | 18.4 | 10945 | 7305 | 5870 | 6598 | 18955 | 8250 | 7275 | 7748 |
| St 5 | 9.5 | 16.6 | 6.8 | 5.7 | 2451 | 2725 | 2815 | 3688 | 3035 | 2850 | 3145 | 4442 |
| St 6 | 11.1 | 17 | 12.3 | 16.5 | 20966 | 24050 | 18600 | 10479 | 26600 | 29050 | 25100 | 25756 |
| St 8 | 19.2 | 17 | 9.8 | 14.3 | 7083 | 5560 | 2855 | 3454 | 9430 | 7130 | 3740 | 4397 |
| St 9 | 10.6 | 13.5 | 9.2 | 9.9 | 5508 | 15800 | 9420 | 14108 | 7035 | 16600 | 13350 | 19833 |
| St 10 | 12.6 | 10.4 | 9.3 | 16.0 | 2841 | 4810 | 2660 | 3765 | 3880 | 6350 | 3175 | 5322 |
| St 11 | 11.3 | 7.4 | 8.6 | 4.9 | 3347 | 6170 | 4425 | 3979 | 2870 | 6625 | 5120 | 5862 |
| St 12 | 7.6 | 10 | 8.7 | 17.4 | 4240 | 7850 | 3920 | 4795 | 6130 | 9440 | 4750 | 5967 |
| St 13 | 6.8 | 5.1 | 7.8 | 16.1 | 1601 | 3945 | 2250 | 4178 | 3510 | 4350 | 3230 | 6050 |
| St 14 | 6.4 | 7.3 | 10.5 | 14.4 | 5219 | 6690 | 6300 | 3976 | 8685 | 7650 | 8335 | 5742 |
| St 15 | 10.8 | 15.7 | 9.6 | 9.3 | 8276 | 20850 | 13500 | 24141 | 9545 | 22300 | 21100 | 40601 |
| St 16 | 12.8 | 17.3 | 8.3 | 16.5 | 8798 | 10750 | 6720 | 8007 | 19200 | 13550 | 8745 | 13756 |
| St 17 | 7.3 | 5.3 | 9.5 | 15.2 | 10092 | 13250 | 12975 | 7478 | 15100 | 15350 | 21150 | 8539 |
| St 18 | 8.1 | 9 | 7.5 | 9.4 | 7235 | 11485 | 7705 | 7736 | 14100 | 12610 | 9550 | 11258 |
| St 19 | 14.4 | 12.4 | 7.9 | 12.7 | 3983 | 3065 | 8330 | 5241 | 5810 | 3870 | 10345 | 7614 |
| St 20 | 9.5 | 10.1 | 8.5 | 7.9 | 4725 | 6430 | 5480 | 3582 | 5455 | 7885 | 5845 | 4579 |
| St 21 | 32.3 | 14.8 | 20.4 | 23.1 | 2863 | 8865 | 5310 | 2942 | 16850 | 9933 | 5980 | 3910 |
| Min | 5.1 | 5.1 | 5.2 | 4.9 | 1601 | 2725 | 2250 | 2942 | 2555 | 2850 | 3145 | 3910 |
| Max | 32.3 | 17.3 | 21.2 | 23.1 | 20966 | 24050 | 18600 | 24141 | 26600 | 29050 | 25100 | 40601 |
| Median | 10.05 | 10.25 | 8.95 | 14.4 | 4972 | 6560 | 5395 | 4744 | 7485 | 7813 | 6065 | 6008 |
| Mean | 11.3 | 11.3 | 10.0 | 13.0 | 6082 | 8823 | 6530 | 6788 | 9528 | 10236 | 8824 | 10081 |
| St Dev | 6.0 | 4.1 | 4.0 | 4.9 | 4423 | 5750 | 4268 | 4980 | 6751 | 6498 | 6474 | 9096 |
| % CV | 53% | 37% | 40% | 37% | 73% | 65% | 65% | 73% | 71% | 63% | 73% | 90% |

Table 5.14  Comparison of Average Metal Concentrations, Central Azeri Surveys 2004, 2006, 2008 and 2010 (μg.g-1) Continued

|  | Cd | Cr | Cu |
| --- | --- | --- | --- |
|  | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 |
| St 1 | 0.14 | 0.47 | 0.31 | 1.01 | 37 | 34 | 37.2 | 45.7 | 24.8 | 17.5 | 17.7 | 22.5 |
| St 2 | 0.15 | 0.37 | 0.24 | 0.90 | 44.1 | 29.3 | 43 | 42.9 | 29.2 | 16.3 | 20.5 | 20.8 |
| St 3 | 0.13 | 0.33 | 0.29 | 1.17 | 37.8 | 38.9 | 47.9 | 47.2 | 17.6 | 19.5 | 19.1 | 24.5 |
| St 4 | 0.12 | 0.41 | 0.35 | 1.01 | 43.3 | 45.7 | 45.3 | 44.3 | 27.2 | 21.1 | 22.6 | 20.3 |
| St 5 | 0.14 | 0.22 | 0.29 | 0.91 | 35.5 | 45.4 | 47 | 57.7 | 15.2 | 21.5 | 22.8 | 24.1 |
| St 6 | 0.19 | 0.76 | 0.71 | 1.67 | 36.3 | 39.1 | 39.7 | 46.0 | 21.7 | 21.5 | 23.6 | 25.8 |
| St 8 | 0.21 | 0.25 | 0.2 | 0.54 | 32.4 | 39.2 | 49.7 | 60.1 | 25 | 19.7 | 18.2 | 27.0 |
| St 9 | 0.2 | 0.43 | 0.54 | 1.62 | 34.6 | 40.3 | 44.7 | 42.6 | 19.9 | 20.7 | 24 | 26.4 |
| St 10 | 0.13 | 0.19 | 0.24 | 0.61 | 26.9 | 33.7 | 44.3 | 35.2 | 10.9 | 12.1 | 17.1 | 11.1 |
| St 11 | 0.14 | 0.29 | 0.38 | 0.36 | 40.6 | 54.4 | 51.1 | 47.6 | 11.2 | 27.4 | 24.5 | 24.0 |
| St 12 | 0.18 | 0.43 | 0.34 | 0.63 | 26.5 | 33.7 | 49.9 | 36.2 | 16.1 | 21.4 | 21.7 | 20.1 |
| St 13 | 0.19 | 0.33 | 0.25 | 0.79 | 33.6 | 40.1 | 55.7 | 39.8 | 16.5 | 23.2 | 22.2 | 20.0 |
| St 14 | 0.17 | 0.37 | 0.43 | 0.47 | 40.7 | 43.7 | 64 | 56.3 | 26.6 | 20.9 | 26 | 24.5 |
| St 15 | 0.2 | 0.67 | 0.48 | 2.43 | 31.2 | 37.5 | 51.5 | 44.1 | 16.9 | 20.7 | 25.4 | 26.9 |
| St 16 | 0.22 | 0.54 | 0.41 | 0.84 | 30.4 | 31.7 | 45.1 | 43.6 | 16.3 | 17.6 | 21.4 | 25.5 |
| St 17 | 0.2 | 0.6 | 0.43 | 0.66 | 34.5 | 45 | 51.3 | 51.2 | 15.2 | 25.1 | 27.2 | 23.6 |
| St 18 | 0.2 | 0.59 | 0.28 | 0.66 | 30.6 | 43 | 42.2 | 35.3 | 26.5 | 27 | 22.6 | 17.4 |
| St 19 | 0.15 | 0.29 | 0.42 | 0.99 | 40.3 | 53.1 | 42.1 | 38.5 | 15.6 | 27.6 | 28.6 | 17.2 |
| St 20 | 0.14 | 0.39 | 0.32 | 0.81 | 27.1 | 34.9 | 38.3 | 41.1 | 21 | 17.3 | 18.7 | 20.0 |
| St 21 | 0.1 | 0.33 | 0.4 | 0.47 | 24.8 | 48.6 | 54.2 | 60.1 | 11.6 | 27 | 30.9 | 28.0 |
| Min | 0.1 | 0.19 | 0.2 | 0.36 | 24.8 | 29.3 | 37.2 | 35.2 | 10.9 | 12.1 | 17.1 | 11.1 |
| Max | 0.22 | 0.76 | 0.71 | 2.43 | 44.1 | 54.4 | 64 | 60.1 | 29.2 | 27.6 | 30.9 | 28.0 |
| Median | 0.16 | 0.38 | 0.345 | 0.82 | 34.6 | 39.7 | 46.2 | 44.2 | 17.3 | 21 | 22.6 | 23.8 |
| Mean | 0.165 | 0.413 | 0.37 | 0.93 | 34.4 | 40.6 | 47.2 | 45.8 | 19.3 | 21.3 | 22.7 | 22.5 |
| St Dev | 0.03 | 0.15 | 0.12 | 0.49 | 5.7 | 6.8 | 6.5 | 7.77 | 5.69 | 4.11 | 3.70 | 4.16 |
| % CV | 21% | 37% | 33% | 53% | 17% | 17% | 14% | 17% | 30% | 19% | 16% | 19% |

Table 5.14 Comparison of Average Metal Concentrations, Central Azeri Surveys 2004, 2006, 2008 and 2010 (μg.g-1) Continued

|  | Fe | Hg | Mn |
| --- | --- | --- | --- |
|  | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 | 2006 | 2008 | 2010 |
| St 1 | 17508 | 25350 | 24450 | 26785 | 0.07 | 0.052 | 0.043 | 0.132 | 331 | 362 | 423 |
| St 2 | 18716 | 19350 | 21850 | 22338 | 0.04 | 0.032 | 0.027 | 0.036 | 313 | 358 | 382 |
| St 3 | 18642 | 26250 | 27300 | 24082 | 0.15 | 0.027 | 0.037 | 0.059 | 346 | 413 | 454 |
| St 4 | 24927 | 25700 | 33100 | 25513 | 0.19 | 0.029 | 0.033 | 0.058 | 349 | 467 | 461 |
| St 5 | 19521 | 29000 | 26700 | 28820 | 0.06 | 0.021 | 0.023 | 0.041 | 512 | 381 | 407 |
| St 6 | 19417 | 28100 | 27150 | 24622 | 0.14 | 0.04 | 0.044 | 0.054 | 388 | 385 | 438 |
| St 8 | 22405 | 29650 | 27750 | 30369 | 0.27 | 0.022 | 0.024 | 0.121 | 363 | 385 | 518 |
| St 9 | 19461 | 27600 | 26850 | 23567 | 0.14 | 0.032 | 0.029 | 0.094 | 342 | 375 | 361 |
| St 10 | 18699 | 23250 | 26150 | 23240 | 0.11 | 0.045 | 0.021 | 0.091 | 329 | 389 | 331 |
| St 11 | 22542 | 28300 | 26300 | 24102 | 0.21 | 0.034 | 0.03 | 0.106 | 431 | 420 | 437 |
| St 12 | 16260 | 22100 | 26450 | 21682 | 0.21 | 0.035 | 0.034 | 0.035 | 332 | 414 | 356 |
| St 13 | 17374 | 23850 | 28800 | 23356 | 0.17 | 0.029 | 0.028 | 0.037 | 330 | 389 | 384 |
| St 14 | 19896 | 24150 | 31100 | 26415 | 0.1 | 0.033 | 0.031 | 0.037 | 386 | 493 | 403 |
| St 15 | 16982 | 26100 | 26600 | 23514 | 0.16 | 0.047 | 0.032 | 0.037 | 332 | 413 | 398 |
| St 16 | 18235 | 25050 | 25600 | 25342 | 0.15 | 0.035 | 0.03 | 0.037 | 342 | 373 | 363 |
| St 17 | 18406 | 23300 | 27450 | 26495 | 0.15 | 0.063 | 0.052 | 0.027 | 411 | 491 | 411 |
| St 18 | 17006 | 23900 | 22700 | 19761 | 0.16 | 0.052 | 0.03 | 0.041 | 390 | 397 | 364 |
| St 19 | 21828 | 30600 | 24500 | 20920 | 0.11 | 0.016 | 0.032 | 0.028 | 500 | 396 | 353 |
| St 20 | 17811 | 23200 | 22950 | 22744 | 0.15 | 0.037 | 0.025 | 0.035 | 356 | 354 | 367 |
| St 21 | 18147 | 27600 | 32350 | 35184 | 0.09 | 0.034 | 0.021 | 0.031 | 607 | 540 | 624 |
| Min | 16260 | 19350 | 21850 | 19761 | 0.04 | 0.016 | 0.021 | 0.027 | 313 | 354 | 331 |
| Max | 24927 | 30600 | 33100 | 35184 | 0.27 | 0.063 | 0.052 | 0.132 | 607 | 540 | 624 |
| Median | 18671 | 25525 | 26650 | 24092 | 0.15 | 0.034 | 0.03 | 0.039 | 352.5 | 393 | 400 |
| Mean | 19189 | 25620 | 26805 | 24943 | 0.14 | 0.04 | 0.03 | 0.057 | 384.5 | 410 | 412 |
| St Dev | 2198 | 2824 | 2937 | 3509 | 0.06 | 0.011 | 0.008 | 0.033 | 75.8 | 50 | 67 |
| % CV | 11% | 11% | 11% | 14% | 39% | 32% | 25% | 58% | 20% | 12% | 16% |

Table 5.14 Comparison of Average Metal Concentrations, Central Azeri Surveys 2004, 2006, 2008 and 2010 (μg.g-1) Continued

|  | Pb | Zn |
| --- | --- | --- |
|  | 2004 | 2006 | 2008 | 2010 | 2004 | 2006 | 2008 | 2010 |
| St 1 | 10.2 | 16.9 | 18.7 | 15.8 | 45.6 | 43.6 | 54.1 | 56.5 |
| St 2 | 6.9 | 13 | 14.7 | 10.1 | 51.3 | 39.7 | 55.7 | 47.5 |
| St 3 | 16.4 | 16 | 14.6 | 17.8 | 52.5 | 44.6 | 61 | 56.3 |
| St 4 | 14.3 | 14.7 | 20.5 | 14.8 | 59.9 | 50.6 | 67.5 | 49.7 |
| St 5 | 12 | 13 | 16.5 | 12.8 | 47.8 | 53.3 | 63.4 | 62.3 |
| St 6 | 21.4 | 24.6 | 28.5 | 22.0 | 63.7 | 52.6 | 60.7 | 56.4 |
| St 8 | 17.3 | 17.5 | 15 | 12.0 | 47.6 | 49.2 | 57.9 | 68.9 |
| St 9 | 14.7 | 19.6 | 21.3 | 18.4 | 49.8 | 55.6 | 69.7 | 70.1 |
| St 10 | 17.1 | 13.3 | 14.9 | 12.4 | 44.5 | 39.7 | 55.4 | 42.1 |
| St 11 | 17.1 | 16.5 | 18.2 | 11.4 | 56.6 | 60.2 | 63.2 | 52.8 |
| St 12 | 25.1 | 16.5 | 18.6 | 12.6 | 46.1 | 43.3 | 61.9 | 44.1 |
| St 13 | 13.7 | 14.1 | 14.7 | 13.9 | 49.2 | 47.4 | 62.2 | 50.6 |
| St 14 | 17.1 | 14.5 | 20.2 | 12.0 | 56.8 | 49.9 | 71.9 | 60.1 |
| St 15 | 20.4 | 24.9 | 22 | 25.3 | 50 | 47.3 | 62.6 | 59.2 |
| St 16 | 20 | 17.5 | 17.2 | 16.6 | 50.9 | 42.8 | 57.2 | 56.3 |
| St 17 | 24.9 | 17.8 | 25.9 | 14.7 | 55.9 | 52.2 | 68 | 56.1 |
| St 18 | 10.3 | 17.6 | 19.7 | 12.0 | 52.8 | 52.9 | 55.1 | 43.6 |
| St 19 | 11.4 | 12.8 | 23.2 | 12.1 | 52.5 | 59.6 | 60.9 | 42.5 |
| St 20 | 19.5 | 15 | 19.3 | 11.1 | 44.2 | 48.1 | 53.7 | 91.0 |
| St 21 | 12.5 | 16 | 22.5 | 13.1 | 38.6 | 55.9 | 66.8 | 61.6 |
| Min | 6.9 | 12.8 | 14.6 | 10.1 | 38.6 | 39.7 | 53.7 | 42.1 |
| Max | 25.1 | 24.9 | 28.5 | 25.3 | 63.7 | 60.2 | 71.9 | 91.0 |
| Median | 16.8 | 16.3 | 19 | 13.0 | 50 | 50 | 61 | 56 |
| Mean | 16.1 | 16.6 | 19.3 | 14.5 | 51 | 49 | 61 | 56 |
| St Dev | 4.9 | 3.4 | 3.9 | 3.9 | 5.9 | 6.0 | 5.4 | 11.5 |
| % CV | 30% | 20% | 20% | 27% | 12% | 12% | 9% | 20% |

## Metal Summary

For the majority of metals (As, Cr, Cu, Fe, Mn, Zn) the data show no clear trends or gradients which could be associated with platform activities.  Iron concentrations increased by approximately 50% between 2004 and 2006, but have not changed markedly since 2006.

Cadmium and mercury concentrations have increased considerably across the survey area between 2008 and 2010, whilst barium and lead concentrations have predominantly decreased over the same period.  However, over the period 2004-2010, mercury concentrations have decreased at all but one station.  The survey-to-survey differences in mercury concentration appear to be too large, and too wide-spread, to be attributable to any point-source contamination.

Three elements, barium, cadmium and lead, exhibited very similar concentration patterns.  These were the only elements which indicated a ‘footprint’ which was spatially related to the platform location.  A similar association was evident in the 2008 data, although the 2008 ‘footprint’ was not congruent with the 2010 footprint (oriented to the SW in 2008 and to the NW in 2010, although this difference is probably due to random variation at a small number of stations).  What is common to both surveys is the persistence of association between these three elements, and the presence of consistently high concentrations of all three at stations 6, 9 and 15.

Barium, when measured by fusion, is considered to be a reliable indicator of the presence of water-based drilling muds discharged with or without associated cuttings.  It is not possible, on the basis of the survey data alone, to determine whether the association with cadmium and lead is

- an indication of contamination present in the drilling mud or

- evidence of higher lead and cadmium concentrations in subsurface rock strata which are subsequently discharged as cuttings or

- evidence of an effect of the presence of cuttings or drilling fluid components on the extractability or analysis of cadmium and lead or

- a coincidence which might not be repeated in subsequent surveys